Computer Electronics
Computer Electronics
Lecture 6: Design Choices

---
How to choose a processor
How to choose a processor
- The envisaged application dictates the choice
- Buy one: microcontroller (PIC, Motorolla), DSP (Texas), GPP (ARM), GPU (Nvidia),…
- Make one

---
Advantages of selecting a GPP
Buy a processor
- Low NRE cost and short development time but:
  - Flexibility?
  - Low unit cost?
  - Performance?
  - Power /energy?
  - Size?

---
ASSPs
ASSPs
- When GPPs are unsuitable, Application Specific Standard Products (ASSPs) are good solution
- An ASSP is an integrated circuit specific for a wide market applications (eg.: video coding)
- Cost is low since production volume is high and performance for that particular application

---
DSPs, GPUs
DSPs, GPUs
- In some cases your application can run well using a Digital Signal Processor (eg.: widely used for audio apps)
- In other cases GPUs can do it: many AI algorithms now use GPUs

---
Microcontrollers (mCs)
Microcontrollers (mCs)
- Target control applications
- Have analog I/Os (internal ADCs and DACs)
- Have digital I/Os: RS232, USB, I2C, SPI and CAN.
- Using a mC avoids developing hardware for the above interfaces

---
FPGAs and ASICs
Make a processor
- FPGA or ASIC?
  - FPGA if volume is low, frequency is low, cost and power not important
  - ASIC if volume is high, frequency is high, cost and power important
- Possible strategy: prototype in FPGA, release FPGA, later release hybrid and finally release ASIC
- Xilinx EasyPath program: create an ASIC/FPGA hybrid

---
Dedicated processors as ASICs
ASICs
- Developed from scratch: high NRE
- Function is well defined
- Cannot be changed after fabrication
  - Make sure to embed some configurability and programmability to reduce risk
- Market must be big to amortize NRE
- Reward: optimal performance, area and power consumption

---
Development stages
Development stages
- Top-down design: natural language, drawings, pseudo-code, etc
- Identify components to buy
- Separate hardware and software functions
- Hardware and software architectures
- Detailed bottom-up design: hardware modules, software classes
- Compile / synthesize: executable / circuit

---
Specification
Specification
- Analyze needed functionalities using market and designer input and create set of specs
- Customers always want everything, now and for free
  - What they will use it for is what matters
- Designers always think they have time to design everything
  - Manage by saying “don’t do”

---
The specs
The specs
- Ordered by importance
- Compatible with product features
- Non conflicting
- Unambiguous

---
Hardware/software co-design
Hardware/software co-design
- Today chips are complex (SoCs)
- SoCs employ a number of standard processors and custom hardware
- Hardware and software development can happen in parallel
- SW can be tested before having HW by using simulators and emulators

---
EU environmental compliance directives
EU environmental compliance directives
- Directive 2002/95 / EC, known as RoHS (Restriction of Certain Hazardous Substances), prohibits the use of cadmium, mercury, hexavalent chromium, polybrominated biphenyls, diphenyl polybrominated ethers and lead.
- Directive 2002/96 / EC, known as WEEE (Waste from Electrical and Electronic Equipment), on the other hand, gives manufacturers responsibility for the reuse or destruction of discarded electrical and electronic products.

---
User interface (UI)
User interface (UI)
Some embedded systems barely need a UI
  - Internal processors and complex circuits get unnoticed by user
- Other systems require a complex UI
  - Developed by engineers, psychologists, designers, etc

---
UI importance
UI importance
- Engineers: can adapt to clumsy UI and not notice
- Users: UI should reflect intention
- UI can make/break products
  - powerful products with few users (Linux?)
  - bad products with many users (Windows?)

---
Documentation
Documentation
- Bad practice: build the whole system then write docs
  - details missed
- Good practice: test and document each submodule
- Use documents of submodules to produce top-level doc
  - Circuit design practices apply to docs (use Latex)

---
Documents for engineers
Document users
- Present and future team members
- Customers and other users
- Time invested in docs always returns
  - Bad docs lead to redesign

---
Document types for engineers
Document types
- Specification document
- Schematics
- Makefile, README files and code comments
- Datasheets (also for users)
- User manuals (also for users)
- Product briefs (marketing)

---
Worksheet 6
- Create a N-bit adder FPGA IP core
- Verilog source code + implementation script /makefile
- Testbench + simulation script / makefile
- Datasheet
  - Overview: short summary
  - Symbol: box with all inputs and outputs
  - Table of parameters: name | description
  - Table of signals: name | direction | description