Computer Electronics
Computer Electronics
Lecture 9: Dedicated Processors

---
Why design a dedicated processor
Why design a dedicated processor
- Not needed for anything else
- No or limited programmability needed
- Can reduce cost in volume production
- Can reduce power/energy consumption
- Better form factor (size matters)
- Has a simpler user interface

---
Dedicated processors combined with GPPs
Dedicated processors combined with GPPs
- Very often the case
- PCIe cards
- Graphics cards
- Surveillance equipment
- Audio equipment
- Etc.

---
Design of dedicated processors
Design of dedicated processors
Data and control paths

---
Design methodology or Art
Design methodology or Art
- Describe the algorithm
- High-level textual description
- Block diagrams
  - High-level: data and control paths
- Pseudo-code for control path
- IO signals: name, width, direction (I,O,IO), description
- Registers: name, direction (Read, Write, RW), description
- Memories: name, function (instructions, data, ..), volatile/non volatile, type (ROM,EPROM,RAM,reg file), Embedded/external, ports (single, dual, two-port, dual-port
  - Holy Grail of Computing: N-port memory!!!
- Data streams: name, description, width, continuous/interrupted
- Busses: name, purpose, type (ISA, AXI, Wishbone, )
- Timing diagrams

---
Design example: dedicated processor that computes pq
Design example: dedicated processor that computes pq
- p is a streaming input (volatile in C language)
- Textual description already given
- Many possible architectures
- Many possible trade-offs…
- Let’s get to the block diagram

---
Parallel architectures
Parallel architectures
p
p
X
X
X
X
X
X
q mults
X
X
X
Tree structure
Linear array
Same throughput lower latency

---
Data valid signals
Data valid signals
Interesting online tool: http://wavedrom.com/editor.html

---
Propagation of the valid signal
Propagation of the valid signal
p
p
X
X
X
X
X
X
q mults
X
Distributed light control
X
X
Tree structure
Linear array
Same throughput lower latency

---
Serial architecture: block diagram
Serial architecture: block diagram
fifo_in_write
Mult
FIFO_IN
x=p
fifo_full_full
fifo_in_empty
fifo_in_read
cnt_start
Counter
Control
rst_reg
cnt_en
cnt_done
reg (q*W bits)
reg_en
reset
fifo_out_write
fifo_out_full
fifo_out_empty
FIFO
y=pq
reg_out
fifo_out_read

---
Design control circuit
Design control circuit
- Flowchart … better for software
- State transition diagram or table
- Pseudo-code
- Experienced designer: HDL (Verilog, VHDL, etc)

---
Controller canonical form
Controller canonical form
Inputs
Combinatorial circuit
Outputs
Current state
State register
Next state

---
State transition diagram
State transition diagram
fifo_in_empty=1
reset=1
(reg=1, cnt=0)
Unknown
Init
fifo_in_empty=0/fifo_in_read=1, reg_en=1,
cnt_start=1, cnt_en=1
Accumulate
fifo_in_empty=1/reg_en=0,
        cnt_en=0
cnt_done=0,fifo_in_empty=0/
cnt_start=1, rst_reg=1,
Pause
fifo_in_empty=0/
fifo_in_read=1,
cnt_en=1, reg_en=1
cnt_done=1, fifo_in_empty=1/
reg_en=0, cnt_en=0

---
State transition table (very incomplete… no space!)
State transition table (very incomplete… no space!)
state	Inputs				Outputs			Next state
st	reset	cnt_done	fifo_in_empty	fifo_out_full	fifo_in_read	fifo_out_write	Reg_en	nxt_st
?	1	-	-	-	-	-	-	init
Init	0	0	1	0	0	0	0	init
Init	0	0	0	0	1	0	0	Accumulate
Accumulate

---
Next steps
Next steps
- Write HDL code (say Verilog)
- Run synthesis
  - Compiles Verilog and produces a generic netlist (gates and flip-flops not related to technology)
- Run mapping
  - Converts generic netlist into technology dependent netlist using component library
- Run place and route
  - Places cells and wire connections into layout
- If user constraint violations tweak design or tool options and rerun
- Complex tools: full configuration requires scripting (in tcl normally)
- A competent designer or design manager can earn a few hundred K/year

---
Worksheet #9
Exercise
Design a dedicated processor that computes the dot product of two streaming vectors