Computer Electronics
Computer Electronics
Lecture 8: Adder Circuits – Part 2

---
Ripple Carry Adder problem: how long will it take for the carry to ripple?
Answer: it will take the time to traverse all single bit adder blocks…. !

---
The Carry Look-ahead Adder (CLA)
The Carry Look-ahead Adder (CLA)
- Speeds up carry computation by using a tree structure instead of a linear structure
- Linear structure length: N
- Tree structure height: log(N)
- Think of N=1000…. Dramatic speedup!

---
Carry prediction from inputs
Carry prediction from inputs
Death
Propagation
Generation

---
Mathematically
Mathematically

---
Carry recursive computation
Carry recursive computation
Can use a 2-level SUM OF PRODUCTS circuit
Multi-input OR and AND gates
Implement as 2-input gate trees!
CARRY AS TREE FUNCTION OF ALL INPUTS!

---
Block Carry Look-ahead Adder
Block Carry Look-ahead Adder
Combine CLA and RCA

---
Using multiple levels
Using multiple levels

---
Tree Carry Look-Ahead Adder
Tree Carry Look-Ahead Adder

---
Tree Carry Look-Ahead Adder
Tree Carry Look-Ahead Adder

---
Tree Carry Look-Ahead Adder
Carry Look-Ahead Tree

---
Carry out of a block
Carry out of a block

---
4-bit CLA
b3
b0
a3
b1
a0
a1
b2
a2
s0 = a0 XOR b0 XOR c0
p0 = a0 XOR b0
g0 = a0*b0
c0
c2
c1
c3
s3
s2
s1
s0
g3
g2
g1
g0
p3
p2
p1
p0
P1,0 = p1*p0
G1,0 = g1+p1*g0
c1 = g0+p0*c0
P3,2
G3,2
P1,0
G1,0
P3,0=P3,2*P1,0
G3,0=G3,2+P3,2*G1,0
c2 = G1,0+P1,0*c0
c4 = G3,0+P3,0*c0
c4
Critical Path Length = 2 * log(N) * (Node delay)

---
Worksheet 8: design this Verilog
b3
b0
a3
b1
a0
a1
b2
a2
s0 = a0 XOR b0 XOR c0
p0 = a0 XOR b0
g0 = a0*b0
c0
c2
A
c1
c3
s3
s2
s1
s0
g3
g2
g1
g0
p3
p2
p1
p0
P1,0 = p1*p0
G1,0 = g1+p1*g0
c1 = g0+p0*c0
B
P3,2
G3,2
P1,0
G1,0
P3,0=P3,2*P1,0
G3,0=G3,2+P3,2*G1,0
c2 = G1,0+P1,0*c0
c4 = G3,0+P3,0*c0
C
c4
Critical Path Length = 2 * log(N) * (Node delay)