Computer Electronics
Computer Electronics
Lecture 7: Multiplier Circuits – Part 2

---
Lecture outline
Lecture outline
- Subtraction
- Sign-extension
- Signed multiplication
- Add-Shift multiplier
- Radix-2 Booth multiplier
- Radix-4 Both multiplier

---
Subtraction: fundamentals
Subtraction: fundamentals
- Adder circuits work equally well with unsigned and signed numbers
- A-B = A + (-B)
  - To subtract simply add the symmetric
  - Symmetric is 2’s complement
  - Easiest way to compute 2’s complement in hardware
    - Complement and add 1

---
Subtraction: circuit
Subtraction: circuit

---
Sign extension
Sign extension
- Sometimes there’s need to increase the number of bits for number representation
- Sign of the number should be preserved
- Q1: represent signed number 1000 (810) with 8 bits
- A1: 11111000 (sign extension in red)
- Q2: represent signed number 0111 (710) with 8 bits
- A2: 00000111(sign extension in red)

---
Logical/Arithmetic right shift
Logical/Arithmetic right shift
- Shifting a number left by p positions is the same as multiplying it by 2p
- Shifting a signed number right by p positions is the same as dividing it by 2p
- Sign must me preserved: arithmetic right shift
- 1000 (-810) shift right by 2 (divide by 4)
  - Logical right shift 0010 (210): wrong!
  - Arithmetic right shift 1110 (-210): correct!

---
Signed multiplication: fundamentals
Signed multiplication: fundamentals
- A = a3 a2 a1 a0, B = b3 b2 b1 b0
- In decimal notation
B = -b3*23 + b2*22 + b1*21 + b0*20
A*B = A * [-b3*23+ b2*22 + b1*21 + b0*20]
Algorithm:
  - Add least significant partial products, subtract most significant partial product

---
Signed multiplication: circuit
1
Signed multiplication: circuit
a3b0
a2b0
a1b0
a0b0
a3b1
a2b1
a1b1
a0b1
FA
FA
FA
HA
a3b2
a2b2
a1b2
a0b2
FA
FA
FA
HA
a3b3
a2b3
a1b3
a0b3
FA
FA
FA
FA
1
p7
p6
p5
p4
p3
p2
p1
p0

---
Add-shift multiply: fundamentals
Add-shift multiply: fundamentals
- Use accumulator register
- Successively add and shift the partial products
- Multiplication ready after N partial products are accumulated
- One accumulation per clock cycle

---
Add-shift multiply: circuit
Add-shift multiply: circuit
/Sub/Nop

---
Add-shift signed multiply: example
Add-shift signed multiply: example
Clock cycle	Product /multiplier reg	Comments
0	00000010	Initial: P=0, m=0010
1	00000001	Nop, SRA
2	11001000	Add M, SRA
3	11100100	Nop, SRA
4	11110010	Subtract M, SRA
M=-710=1001 , m=210=0010
M*m = -1410 = 11110010

---
Booth multiply
Booth multiply
Andrew Donald Booth
  - British electrical engineer, physicist and computer scientist
  - Early developer of the magnetic drum memory for computers
  - Invented Booth's multiplication algorithm.

---
Booth multiply: observation
Booth multiply: observation
Multiply by small positive numbers is fast because of many leading 0s
  - Example: multiply by 00000011 (310)
  - Only 2 non-zero partial products
  - Computation can stop after the 2 partial products are accumulated

---
Booth multiply: negative numbers
Booth multiply: negative numbers
Similar observation for small negative numbers
  - Many leading 1s: 11111100 (-410)
- Add-shift multiply: many partial products to add!
- Booth’s idea: recode the multiplier

---
Booth recoding
Booth recoding
- 00111100 = 01000000 - 00000100
- M*00111100 =
– M*00000100 + M*01000000
Partial products reduced from 4 to 2!

---
Booth algorithm
Booth algorithm
With multiplicand M and multiplier m:
1. Scan multiplier m from right to left
2. If 0 to 1 transition in positions p-1 to p:
Subtract M*2p
If 1 to 0 transition in positions q-1 to q:
Add M*2q

---
Booth algorithm: advantages
Booth algorithm: advantages
Worst case: 01010101
#transitions = N, N partial products
No advantage
Average case for random numbers
#transitions = N/2
Half of the additions
Real average case
  - Small numbers common: low #transitions
  - Few additions
- Works for both unsigned and signed numbers!

---
Booth multiply: same circuit, different control
Booth multiply: same circuit, different control
/Sub/Nop

---
Booth implementation: discussion
Booth implementation: discussion
The above implementation does add-shift in the same clock cycle
  - Advances 1 bit per cycle
  - No time advantage for Booth compared to Add-Shift
  - Power advantage? lower node activity…
- How to improve the above implementation
  - Advance by number of trailing 0s or 1s
    - Need Count Leading Zeros (CLZ) hardware: O(N log N)
    - Need Barrel Shifter (BS) hardware: O(N log N)
    - Why not simply use a matrix multiplier?
- Speeds up basic implementations, including assembly ones, that can’t do simultaneous add-shift

---
Booth multiply: example
Booth multiply: example
Clock cycle	Product /multiplier register	Comments
0	00000010(.0)	Initial: P=0, m=0010, T=0.0
1	00000001(.0)	SRA, no transition, T=1.0
2	00111000(.1)	Sub M, RA, T=0.1
3	11100100(.0)	Add M, SRA, T=0.0
4	11110010	SRA
M=-710=1001, -M=0111, m=210=0010
M*m = -7 x 2 = -14, 1001 x 0010 = 11110010

---
Radix-4 Booth multiply
Radix-4 Booth multiply
- Same principle but sequences of 2 bits are analyzed (radix = 22=4)
- Each 2-bits form a quaternary digit
- Advantage: halves the number of partial products

---
Radix-4 Booth algorithm
Radix-4 Booth algorithm
Current digit	Previous bit	Operation
00	0	0-sequence: do nothing
00	1	Ends 1-sequence: +M
01	0	Lonely 1: +M
01	1	Terminal 0: +2M
10	0	Terminal 1: -2M
10	1	Lonely 0: -M
11	0	Ends 0-sequence: -M
11	1	1-sequence: do nothing

---
Radix-4 Booth multiply: example
Radix-4 Booth multiply: example
Clock cycle	Product /multiplier reg	Comments
0	0000000011110110(.0)	Initial: P=0, m=-1010,T=10.0
1	1111101000111101(.1)	, Sub 2M and SRA-2
2	0000010010001111(.0)	T=01.1, Add 2M and SRA-2
3	1111111000100011(.1)	T=11.0, Sub M and SRA-2
4	1111111110001000	T=11.1, SRA-2
M=1210=00001100, m=-1010=11110110
-M =11110100, -2M=11101000, 2M=00011000
1210 * -1010 = -12010 = 10001000

---
Worksheet #7
Worksheet #7
Write a 32-bit Radix-2 Booth Multiplier in Verilog