Computer Electronics
Computer Electronics
Lecture 8: Digital Circuits and Verilog III

---
Verilog/iob-lib: what we have learned
- Create modules with module/endmodule
  - Create interface signals with `INPUT, `OUTPUT, `INOUT
- Instantiate components in modules with component name – instance name – interface signals
- Create registers with `REG
- Create combinational circuits with `COMB

---
Register with enable signal
- `IOB_REG_E(CLK, EN, OUT, IN)
  - CLK: clock signal
  - EN: enable signal
  - OUT: output signal
  - IN: input signal
  - How it works: OUT registers IN at clock rising edge only if EN is asserted, otherwise keeps previous value
- Verilog description of register:
  always @(posedge clk)
  if(en)
  my_reg <= my_reg_next;
- Always: process repeats endlessly; if: like in software but used in hardware descriptions, <= : non-blocking assignment (!)
- Or just use the iob-lib macro:
  `IOB_REG(clk, en, my_reg, my_reg_next)

---
Register with synchronous reset
- `IOB_REG_R(CLK, RST, RST_VAL, OUT, IN)
  - CLK: clock signal
  - RST: synchronous reset signal
  - RST_VAL: value after reset
  - OUT: output signal
  - IN: input signal
  - How it works: if RST is asserted then OUT takes value RST_val on the next clock rising edge; else OUT registers IN at clock rising edge, otherwise keeps previous value

---
Verilog for register with synchronous reset
- Verilog description
  always @(posedge clk)
  if(rst)
  my_reg <= some_init_value;
  else
  my_reg <= my_reg_next;
- Or simply use iob-lib:
  - `IOB_REG_R(clk, rst, some_init_val, my_reg, my_reg_next)

---
Register with enable and synchronous reset
- `IOB_REG_RE(CLK, RST, RST_VAL, EN, OUT, IN)
  - CLK: clock signal
  - RST: synchronous reset signal
  - RST_VAL: value after reset
  - OUT: output signal
  - IN: input signal
  - How it works: if RST is asserted then OUT takes value RST_val on the next clock rising edge; else OUT registers IN at clock rising edge only if enable is asserted, otherwise keeps previous value

---
Verilog for register with enable and synchronous reset
- Verilog description
  always @(posedge clk)
  if(rst)
  my_reg <= some_init_value;
  else if (en)
  my_reg <= my_reg_next;
- Or simply use iob-lib:
  - `IOB_REG_RE(clk, rst, some_init_val, my_reg, my_reg_next)

---
Register with asynchronous reset
- `IOB_REG_AR(CLK, RST, RST_VAL, OUT, IN)
  - CLK: clock signal
  - RST: asynchronous reset signal
  - RST_VAL: value after reset
  - OUT: output signal
  - IN: input signal
  - How it works: if RST is asserted then OUT takes value RST_VAL immediately; else OUT registers IN at clock rising edge, otherwise keeps previous value

---
Verilog for register with asynchronous reset
- Verilog description
  always @(posedge clk, posedge rst)
  if(rst)
  my_reg <= some_init_value;
  else
  my_reg <= my_reg_next;
- Or simply use iob-lib:
  - `IOB_REG_AR(clk, rst, some_init_value, my_reg, my_reg_next)

---
Register with enable and asynchronous reset
- `IOB_REG_ARE(CLK, RST, RST_VAL, EN, OUT, IN)
  - CLK: clock signal
  - RST: asynchronous reset signal
  - RST_VAL: value after reset
  - EN: enable signal
  - OUT: output signal
  - IN: input signal
  - How it works: if RST is asserted then OUT takes value RST_VAL immediately; else if enable is asserted, OUT registers IN at clock rising edge; otherwise keeps previous value

---
Verilog for register with enable and asynchronous reset
- Verilog description
  always @(posedge clk, posedge rst)
  if(rst)
  my_reg <= some_init_value;
  else if (en)
  my_reg <= my_reg_next;
- Or simply use iob-lib:
  `IOB_REG_ARE(clk, rst, some_init_value, en, my_reg, my_reg_next)

---
Simple counter
- `IOB_COUNTER(CLK, CNT): free running, no reset => IMPOSSIBLE TO SIMULATE!!!
- `IOB_COUNTER_R(CLK, RST, CNT)
  - CLK: clock signal
  - RST: synchronous reset signal
  - CNT: counter signal
  - How it works: if RST is asserted CNT will be 0 on the next clock rising edge; otherwise CNT will be incremented by one on the next clock rising edge.
- Verilog description of counter:
  always @(posedge clk)
  if(rst)
  my_cnt <= 0;
  else
  my_cnt <= my_cnt+1;
- Or just use iob-lib:
  `IOB_COUNTER_R(clk, rst, my_cnt)

---
Other counter types
- `IOB_COUNTER_RE(CLK, RST, EN, CNT)
- `IOB_COUNTER_AR(CLK, RST, CNT)
- `IOB_COUNTER_ARE(CLK, RST, EN, CNT)
- `IOB_WRAPCNT_R(CLK, RST, CNT, WRAP_VAL)
  always @(posedge clk)
    if(rst)
    my_cnt <= 0;
    else if (cnt == my_wrap_value)
    my_cnt <= 0;
    else
    my_cnt <= my_cnt + 1;
- `IOB_WRAPCNT_RE(CLK, RST, EN, CNT, WRAP_VAL)
- `IOB_WRAPCNT_AR(CLK, RST, CNT, WRAP_VAL)
- `IOB_WRAPCNT_ARE(CLK, RST, EN, CNT, WRAP_VAL)

---
IOb-lib macros for the testbench
- `IOB_CLOCK(CLK_NAME, PER)
  - CLK: Clock name
  - PER: Clock period in units given by the `timescale directive
  - Initial value is 1, first high-low (1→0) transition happens at time PER/2
- `IOB_RESET(RST_NAME, RISE_TIME, DURATION)
  - RST_NAME: reset signal name
  - RISE_TIME: time instant of the first low-high transition
  - DURATION: active reset duration in units given by the `timescale directive

---
The timescale directive
`timescale 1ns/ps
- Used to specify simulation timing
- #<x.y> is a delay of x nanoseconds + y picoseconds (eg. 3.045 ns)
- #<x.y> directives are meaningless and ignored during synthesis; only meaningful in simulation
- In synthesis you cannot force when something will happen
- The most you can do is to impose a time limit, e.g, a clock period
- For example
  `COMB #10 c = a & b;
  simulates an AND gate that responds in 10ns but synthesizes an AND gate that responds whenever the respective physical gate responds

---
Explaining the CLOCK iob-lib macro
- `define IOB_CLOCK(CLK, PER) reg CLK always #(PER/2) CLK = ~CLK
- If you type `IOB_CLOCK(clk, 10) you create a clock signal in the testbench having a period of 10ns
- The `IOB_CLOCK macro does not work in design files that are synthesized, only in simulation
- Synthesis tools cannot implement clocks
- A clock is an oscillator, mostly analog, and has been studied in basic Electronics courses
- However, the synthesis tool needs to know that a signal is a clock in order to impose timing constraints

---
Explaining the RESET iob-lib macro
`define IOB_RESET(RST_NAME, RISE_TIME, DURATION) reg RST=0; \
initial begin #RISE_TIME RST=1; #DURATION RST=0; end
- If you type `IOB_RESET(rst, 10, 20) you create a reset pulse signal in the testbench having a duration of 10ns rising at time 10
- The `IOB_RESET macro does not work in design files that are synthesized, only in simulation
- Synthesis tools cannot implement reset pulses of an arbitrary duration
- A reset signal with an arbitrary duration is implemented by a pulse generator also studied in the basic Electronics courses
- However it is possible to synthesize pulse generators if the duration of the pulse is a multiple of the clock period
- The synthesis tool does need to be told that a signal is an asynchronous reset: it can infer this info from the Verilog code itself

---
The Wavedrom program
- In the iob-soc repo you can see the hardware-software-documentation trichotomy
- Documentation is key to a successful product
- Timing diagrams are a succinct and effective way to document
- However, creating timing diagrams by hand is timing consuming
- One possibility is to simulate and then screen shoot the waveforms into a timing diagram for the documentation
  - Avoids errors: design and documentation become consistent
  - However to update the document, you need to rerun the simulation and repeat the process
- The Wavedrom program, available online and offline is a very productive tool to create complex timing diagrams – visit wavedrom.com
- The input file is a .json file, a user-friendly type of dictionary used in JavaScript and also in Python
- An automation flow consisting of simulation→.vcd file→vcd2wavedrom→wavedrom→png file is possible and is being developed at IObundle