Computer Electronics
Computer Electronics
Lecture 6: Digital Circuits and Verilog

---
Recap: Digital circuits
- Combinational (no feedback paths)
- Sequential (with feedback paths – remembers the past)
  - Asynchronous (no clock signal)
  - Synchronous (with clock signal)
- Asynchronous circuits
  - Very difficult to design: need to account for physical propagation delays and logic glitches
  - Only small designs: latches and flip-flops
- Synchronous circuits
  - Easy to design: propagation delays and glitches are forced out of the equation
    - During the clock period we wait for them to go way!
  - Really large designs: CPUs, GPUs, FPGAs, custom

---
Controller canonical form
Recap: what is inside of a digital circuit?
τP < T
Inputs
Combinatorial circuit
Outputs
Current state
Register
Next state

---
Full Adder logic circuit
Recap: what is a combinatorial circuit?
- Full adder circuit
- Si = Si(ai, bi, ci);
- Ci+1=Ci+1(ai, bi, ci)
Propagation delays!
Glitches!

---
Recap: what is a register
- It is a set of memory elements (flip-flops or latches)
- Latches are transparent, the output changes with the input if enabled: RARELY USED
- Flip-flops are not transparent, the output only changes at on of the active clock signal edge: THEY ARE EVERYWHERE

---
The FLIP-FLOP!
- Only D type is studied
- Verilog description is directly mapped to a library component
- Set (S) and Reset (R) are optional
- It is rare that S and R are simultaneously supported: no library component
- Responds to the rising (positive) edge of the clock (CLK)
- Responds to the falling (negative) edge of the clock if an inverter is placed at the CLK input (DANGER ZONE!)
- The optional Enable signal (EN) determines whether the flip-flop will respond or not to the clock edge
EN
CLK

---
The FLIP-FLOP Timing Diagram
Setup time tS
Hold time tH
NO GLITHES!
T > tS+max(tP,tH)
f < (tS+max(tP,tH))-1
Propagation delay tP

---
Behaviour summary
- The output Q takes the value of the input D at the active clock edge after time tP
- The input D must be stable for at least a time tS before the clock edge
- The input D must be stable for at least a time tH after the clock edge (automatically guaranteed by propagation time)
- Violations of tS and tH result in malfunction!

---
The Flip-flop Set/Reset types
- Asynchronous
  - Output Q responds IMMEDIATELY (after small tP) to assertions of S and R
- Synchronous
  - Output Q responds to S/R assertions present before the clock edge (before tS)

---
The FLIP-FLOP with asynchronus reset

---
The FLIP-FLOP with synchronous reset and enable

---
So let’s learn Verilog! Or NOT!
- The iob-lib repo has gone public as of today!
- The iob-lib repo contains
  - Useful Verilog macros to avoid writing the same Verilog description over and over again
  - Useful components (modules) to avoid writing the same Verilog description over and over again
- Enjoy!

---
Just learn 2 things!
τP < T
- If any digital circuit is just this then you just need to learn to describe:
  - combinatorial circuits
  - registers
- Not bad, is that?
Inputs
Combinatorial circuit
Outputs
Register
Current state
Next state

---
Signal Wires
- Verilog describes circuits
- Circuits are blocks connected by wires that carry digital signals (0 or 1)
- So we need to declare and use wires
- Verilog describes two types of wires: wire and reg
- And the mess begins:
  - A wire is a wire but it cannot be used in all situations
  - A reg is a wire (not a register as the name suggests) but it cannot be used in all situations
- What a start!!!

---
wire versus reg
- So when do we use wire?
  - A component output must be a wire
  - The left hand side of an assign statement must be a wire
  - A resolved signal must be a wire
- So when do we use reg?
  - In the left hand side of expressions inside a process
- So what is assign, resolved signal, process?
- It’s a long story to be made short with iob-lib!