Computer Electronics
Computer Electronics
Lecture 7: Multiplier Circuits – Part 2

---
Lecture outline
Lecture outline
- Subtraction
- Sign-extension
- Signed multiplication
- Add-Shift multiplier

---
Subtraction: fundamentals
Subtraction: fundamentals
- Adder circuits work equally well with unsigned and signed numbers
- A-B = A + (-B)
  - To subtract simply add the symmetric
  - Symmetric is 2’s complement
  - Easiest way to compute 2’s complement in hardware
    - Complement and add 1

---
Subtraction: circuit
Subtraction: circuit

---
Sign extension
Sign extension
- Sometimes there’s need to increase the number of bits for number representation
- Sign of the number should be preserved
- Q1: represent signed number 1000 (-810) with 8 bits
- A1: 11111000 (sign extension in red)
- Q2: represent signed number 0111 (710) with 8 bits
- A2: 00000111(sign extension in red)

---
Logical/Arithmetic right shift
Logical/Arithmetic right shift
- Shifting a number left by p positions is the same as multiplying it by 2p
- Shifting a signed number right by p positions is the same as dividing it by 2p
- Sign must me preserved: arithmetic right shift
- 1000 (-810) shift right by 2 (divide by 4)
  - Logical right shift 0010 (210): wrong!
  - Arithmetic right shift 1110 (-210): correct!

---
Signed multiplication: fundamentals
Signed multiplication: fundamentals
- A = a3 a2 a1 a0, B = b3 b2 b1 b0
- In decimal notation
B = -b3*23 + b2*22 + b1*21 + b0*20
A*B = A * [-b3*23+ b2*22 + b1*21 + b0*20]
Algorithm:
  - Add least significant partial products, subtract most significant partial product

---
Signed multiplication: circuit
1
Signed multiplication: circuit
a3b0
a2b0
a1b0
a0b0
a3b1
a3b1
a2b1
a1b1
a0b1
FA
FA
FA
HA
FA
FA’
a3b2
a3b2
a2b2
a1b2
a0b2
FA
FA
FA
HA
FA’
a3b3
a3b3
a2b3
a1b3
a0b3
FA
FA
FA
FA
FA’
1
p7
p6
p5
p4
p3
p2
p1
p0

---
Add-shift multiply: fundamentals
Add-shift multiply: fundamentals
- Use accumulator register
- Successively add and shift the partial products
- Multiplication ready after N partial products are accumulated
- One accumulation per clock cycle

---
Add-shift multiply: circuit
Multiplicand
register (n)
zeroer
n
i==n
inverter
n
Counter
adder
cin
n
n+1
Product-Multiplier (PM)
Right-Shift register (2n bits)

---
Add-shift signed multiply: example
Add-shift signed multiply: example
Clock cycle	Product /multiplier reg	Comments
0	00000010	Initial: P=0, m=0010
1	00000001	Nop, SRA
2	11001000	Add M, SRA
3	11100100	Nop, SRA
4	11110010	Subtract M, SRA
M=-710=1001 , m=210=0010
M*m = -1410 = 11110010

---
Worksheet 11
- Consider the add-shift multiplier in ecomp/verilog/add_shft_mul.v
- Compile: iverilog add_shft_mul.v
- Run: ./a.out
- Modify the circuit to support signed multiplication, recompile and rerun