Computer Electronics
Computer Electronics
Lecture 2: Iob-SoC Configuration

---
Recap of last lesson: IOb-SoC
CPU
picoRV32
CPU
Wrapper
I/D
Memory Instruction bus
Processor data bus
I/D SPLIT
D/P SPLIT
UART bus
Memory
Memory data bus
UART
Accelerators’ bus
User
Hardware
Accelerator
[Speaker Notes: Let’s simplify the vNA.]

---
Github
Fork
Iob-SoC
fork
IOb-SoC
remote
Push
Pull
Home
Student
device
Student 1
device
Student 3
device
Student Group

---
Quick recap: IOb-SoC
- The PicoRV32 RISC-V CPU (open-source)
- Boot ROM (has small program to load user programs)
- SRAM (on-chip memory for running small programs or storing fast access data)
- Instruction and Data L1 Caches + shared L2 cache
- UART interface for communication
- Other optional modules: Ethernet, UART, DMA
- Ready to attach user modules

---
Quick recap: IOb-SoC
- The PicoRV32 RISC-V CPU (open-source)
- Boot ROM (has small program to load user programs)
- SRAM (on-chip memory for running small programs or storing fast access data)
- Instruction and Data L1 Caches + shared L2 cache
- UART interface for communication
- Other optional modules: Ethernet, UART, DMA
- Ready to attach user modules

---
Make recap, the include directive
  include “my_wonderful_makefile_segment.mk”
  dead: beef.c lib.c
    gcc -o $@ $<
    cat $^
List of dependencies
Target
Recipes
Short for “beef.c”
Short for “beef.c lib.c”
Short for “dead”

---
Iob-SoC Tour
- System configuration

---
Iob-SoC: system configuration
- Accomplished using makefile segment system.mk
  - Located at repo root
- Parameters of most interest in system.mk
  - FIRM_ADDR_W = log2(firmware size in bytes)
  - SRAM_ADDR_W = log2(SRAM size in bytes)
  - PERIPHERALS = list of peripherals

---
system.mk: FIRM_ADDR_W
- Firmware is the resident software of an embedded system
- Sits on non-volatile memory: ROM, EPROM, Flash
- Note the _W suffix: stands for WIDTH in bits
- The firmware bytes can be addressed with FIRM_ADDR_W bits
- Then there are 2FIRM_ADDR_W bytes in the firmware

---
Memory organization for a 32-bit CPU
Byte 3	Byte 2	Byte 1	Byte 0
		...	Byte 4
Byte 23	...
0x00
0x04
0x08
Full word addresses =
Byte address >> 2
0x0C
Half word addresses =
Byte address >> 1
0x10
0x14

---
A 32-bit CPU can
- With single instruction can
  - Read and write single bytes (char, uchar)
  - Read and write single half words (short, ushort)
  - Read and write single long words (int, uint)
- With multiple instructions can
  - Read and write multiple bytes (number array, string)
  - Read and write multiple short words (arrays)
  - Read and write multiple long words (arrays)
- Read = Load, Write = Store

---
system.mk: SRAM_ADDR_W
- The SRAM bytes can be addressed with FIRM_ADDR_W bits
- Then there are 2SRAM_ADDR_W bytes in the firmware
- If the SRAM_ADDR_W is greater than FIRM_ADDR_W then the firmware fits in the SRAM and can run on it

---
system.mk: PERIPHERALS
- List of peripherals in system.mk
- By default contains only one peripheral: the UART
- Users can make peripherals and attach them to the IOb-SoC peripheral bus
- For this to happen the peripheral repository must follow a certain structure

---
Upgrading IOb-SoC with Flash
CPU
picoRV32
CPU
Wrapper
I/D
Memory Instruction bus
Processor data bus
I/D SPLIT
ROM
(bootload)
+
SRAM
(execution
and temp
storage)
D/P SPLIT
UART bus
UART
Accelerators’ bus
Memory data bus
Flash
Memory
[Speaker Notes: Let’s simplify the vNA.]

---
Iob-SoC with FLASH scenario
1. Power on; Hardware reset (hard reset)
2. Bootloader program copied from ROM to SRAM by a special hardware circuit; bootloader runs on SRAM
3. Bootloader awaits for firmware to arrive by UART
4. Bootloader receives firmware from UART and loads it to FLASH
5. Boot loader reboots system (soft reset)
6. Boot loader starts again and awaits for firmware to arrive by UART
7. Bootloader times out and copies firmware from FLASH to SRAM
8. Bootloader sets boot control register and reboots system
9. Boot control register tells bootloader to start running from a different address where firmware has been stored

---
Iob-SoC with default scenario
1. Power on; Hardware reset (hard reset)
2. Bootloader program copied from ROM to SRAM by a special hardware circuit; bootloader runs on SRAM
3. Bootloader awaits for firmware to arrive by UART
4. Bootloader receives firmware from UART and loads it to SRAM
5. Bootloader sets boot control register and reboots system
6. Boot control register tells bootloader to start running from a different address where firmware has been stored

---
Iob-SoC with default scenario
Firmware address (0)
SRAM
3
firmware
CPU
ROM
(bootloader)
Instruction bus
Bootloader address
2
Boot
control
reg
Bootloader
1
Data bus
MEMORY SYSTEM