Computer Electronics
Computer Electronics
Lecture 2: The Verilog Language

---
Digital circuit example
Digital circuit example
data_in_valid
multiplier
data_in (p)
cnt_start
Counter
Control
cnt_en
count
reg (q*W bits)
reg_en
reset
data_out_valid
reg_out
data_out(pq)

---
Tools for circuit simulation
Tools for circuit simulation
- Linux: free OS
- Icarus Verilog: free Verilog simulator
  - http://iverilog.icarus.com/
- GtkWave: free wave visualizer
  - http://gtkwave.sourceforge.net/

---
Testbench and Unit Under Test (UUT)
Testbench and Unit Under Test (UUT)
The testbench
Output
Signal analyzers
Input
UUT
Pass/Fail
Signal sources

---
Design files
Design files
- top.v : the top module
- top_tb.v : the testbench
- register.v : the register module
- counter.v : the counter module
- control.v : the controller module
- Makefile : instructions for compilation and execution