Computer Electronics
Computer Electronics
Lecture 20: Cache

---
Outline
Outline
- Motivation
- The cache concept
- Cache organization
- Directly mapped cache
- Fully associative cache
- K-way associative cache
- Replacement policy
- Write policies

---
Motivation
Motivation
- Accessing main memory (usually external DRAM) is slow due to latency of memory controller and memory itself
- The cache is a smaller SRAM on chip memory that can be accessed in 1 clock cycle preferably
- Typical cache sizes are in the order of 10s of kB
- Data word (32 or 64 bits) accessed using a parallel bus

---
The Cache concept
Cache may have multiple levels successively slower but larger: L1, L2, L3… (2 or 3 levels common
The Cache concept
Cache hit rate = p
Cache miss rate = 1-p
Memory (DRAM)
CPU
Cache
Ta = pTc+(1-p)Tm
Large /slower
Probability of
Data in cache (p): HIGH
Data in memory: MEDIUM
Data in disk: LOW
Small/fast
Principle of LOCALITY
In space: data in near addresses are more likely to be accessed
In time: data recently accessed is more likely to be accessed again
Disk
Very large / very slow

---
Cache organization
Cache organization
Cache line size: n (typically 8 /16 / 32 words)
Main memory address (addr)
Offset
Tag
Set
Set = addr[S-1 -:S_W ]
Tag	Word n-1	…	Word 0
addr[A_W-1 -: T_W]	M[{tag, set, n-1}]		M[{tag, set, 0}]
tag_out[T_W-1:0]
line_out[n*D_W-1:0]

---
Directly Mapped Cache
(each set only has 1 line in cache)
Directly Mapped Cache
Each set only has 1 line in cache
Memory address
Tag	Line
	Wn-1, Wn-2, …, W0
Addressed set
Offset
Tag
Set
Set 1
Set n
==?
Data word
HIT / MISS

---
Fully Associative Cache
(single set, multiple lines)
Fully Associative Cache
(single set, multiple lines)
Memory address
Tag
Line
Tag
Line
…
Tag
Offset
==
==
Encoder
HIT / MISS
Data word

---
K-Way Set Associative Cache
(each set has k lines in cache)
K-Way Set Associative Cache
(each set has k lines in cache)
Tag k	Line k	…	Tag 1	Line 1
0
…
#sets-1
Memory address
Offset
Tag
Set
==?
==?
Line sel
Word sel
logic
Data word
HIT / MISS

---
Number of bits
Number of bits
- #offset bits = log2(#words per line)
- #set index bits = log2(#sets)
- #tag bits =
  #address bits – #offset bits - #set index bits

---
Cache replacement policy
Cache replacement policy
- Upon a cache miss, line must be replaced
- Directly mapped cache (aka 1-way cache)
  - Only one line to choose – no choice
- K-way cache replacement policy
  - Random replace (RR): needs random counter – easy
  - Least recently used (LRU): needs usage record – difficult
  - Pseudo LRU: needs 1 bit for the last used, replace adjacent – easy
  - Most recently used (MRU): needs 1 bit for the last used – easy
  - Least Frequently Used: needs frequency counter – difficult
  - …. 17 policies listed in Wikipedia…

---
Cache write policy
Cache write policy
Write-through
  - data word (not block) is written to cache and main memory in case of a hit (miss case analyzed separately)
- Write-back
  - Data is written to cache only in case of a hit (miss case analyzed separately)
  - Data is written to memory only when line is replaced
  - Performance improvement with Dirty bit
    - Dirty bit is set when line is modified
    - Upon replacement, data is saved in memory only if Dirty bit is set

---
Write through hardware
Write through hardware
Cache
Memory
CPU
Write-through buffer

---
Write-through buffer overflow
Write-through buffer overflow
Memory
Cache L2
CPU
Cache L1
Write-through buffer (FIFO)
Problem: If write frequency greater than word write time to memory than WTB becomes full
Remedy: use 2 cache levels, as writing to L2 cache is faster than writing to memory

---
Cache write miss policy
Cache write miss policy
- What to do when line to write is not in cache
- Write allocate policy
  - Transfer line to cache then write to it
- Write not-allocate
  - Write to main memory only
- Usual policy combination
  - Write-through and write not-allocate
  - Write-back and write allocate