Computer Electronics
Electronic Systems of Computers
Lecture 5: IOb-SoC Purpose, Digital Circuits and Verilog

---
Recap last lesson: the IOb-SoC submodules directory
- System submodules
  - CPU
  - CACHE
  - UART
- A git submodule is a pointer to another git repository
  - Allows for modular and distributed development
  - Easy to add with the git submodule add <url> path/to/the/submodule
  - Easy to remove: git rm path/to/the/submodule
- The way the system collects hardware and software components from the submodules and assembles them in the system is discussed in this lecture.

---
IOb-SoC: use cases
- Tool to develop SoCs
- Tool to develop new processor Peripherals
- Tool to develop new Embedded Software
- Tool to develop interesting new applications that rely on new custom designed hardware blocks

---
IOb-SoC: exploiting parallelism
- Moore’s (INTEL’s co-founder) law is dying (is it?):
  - #transistors per m² is not doubling every 2 years!
  - Frequency of operation is not steadily increasing, it has stagnated
- Huang’s (NVIDIA’s chief) law is being born:
  - GPU performance is doubling every 2 years!
  - A GPU is a many (simple) core solution: exploits parallelism in hardware
- Any parallel design can do the same, not just GPU
- AI and Machine Learning provide plenty of opportunities
- Daniel Garigali & Pedro Miranda Yolo V3 implementation!

---
IOb-SoC: Yolo V3
- CPU is less than 1% of design
- Me: could you use a more powerful CPU?
- Daniel and Pedro: what for? The bottleneck is not the CPU!
- Two brilliant master theses!

---
IOb-SoC: using silicon to do WORK, not management
- CPUs have evolved to use silicon for managing purposes rather than doing the actual work
- Memory management units
- Out of order execution management
- Cache management
- ALU!

---
IOb-SoC: import components with git submodules
- Easy way to import hardware and respective software components into IOb-SoC
- Add peripheral as git submodule in the submodules directory
  - Example: /home/user/sandbox/iob-soc/submodules/TIMER
- In config.mk, add peripheral name to PERIPHERALS list variable
  - PHERIPHERALS := UART TIMER

---
IOb-SoC: how peripherals are imported
- The Makefile inserts peripherals automatically
- Visit hardware.mk
- Visit software.mk:
  - Address structure:
    {Pbit, Slave ID, Not Used, Slave Internal Address}
  - Pbit: 1 bit
  - Slave ID: $clog2(N_SLAVES) bits
  - Slave internal address width: $clog2(#addresses)
    (TIMER_ADDR_W, UART_ADDR_W)
- What do you do next?
  - Test in simulation: short tests with icarus, longer tests with Verilator(!)
  - Test in FPGA: prove in silicon, run longer tests

---
Testbench and Unit Under Test (UUT)
Verilog module (a digital circuit)
Verilog module
A Digital Circuit
Outputs
Inputs
inouts (bidirectional wires)

---
Verilog module (a circuit)
module my_peripheral
   (
    input clk,
    input rst,
    // native bus
    input valid, //denotes a valid read or write operation
    input [`SRAM_ADDR_W-3:0] addr, //address to read or write
    input [`DATA_W-1:0] wdata, //data to be written
    input [`DATA_W/8-1:0] wstrb, //bytes to be written
    output [`DATA_W-1:0] rdata, //data to be read
    output ready //read or write completed and ready for next
);
//description of module goes here
endmodule

---
The testbench
The testbench
Output
Signal analyzers
Input
UUT
Pass/Fail
Signal sources

---
Verilog testbench
(not a real circuit!)
Used in Verilog simulation!
module my_testbench;
//description of test hardware
//instance of the Unit Under Test
endmodule

---
Verilog header files
`include “my_header_file.vh”
// this like the C language #include
module my_testbench;
//description of test hardware
//instance of the Unit Under Test
endmodule

---
Verilog macros
`define X 13
// this like the C language #define
`define SUM(A,B) A+B
//macros with arguments are supported
ATTENTION: macros are not functions!
They are just a clever Cut & Paste mechanism
They are handled by the pre-processor that does the Cut & Paste
assign C = `SUM(A,B);
assign C = A + B;

---
Controller canonical form
What is inside of ANY digital circuit?
Inputs
Combinatorial circuit
Outputs
Current state
Register
Next state

---
Full Adder logic circuit
What is a combinatorial circuit?
- Full adder circuit
- Si = Si(ai, bi, ci);
- Ci+1=Ci+1(ai, bi, ci)
Propagation delays!
Glitches!

---
Propagation delay

---
Combinational glitches!

---
Digital circuits
- Combinational (no feedback paths)
- Sequential (with feedback paths – remembers the past)
  - Asynchronous (no clock signal)
  - Synchronous (with clock signal)
- Asynchronous circuits
  - Very difficult to design: need to account for physical propagation delays and logic glitches
  - Only small designs: latches and flip-flops
- Synchronous circuits
  - Easy to design: propagation delays and glitches are forced out of the equation
    - During the clock period we wait for them to go away!
  - Really large designs: CPUs, GPUs, FPGAs, custom

---
What is a register
- It is a set of memory elements (flip-flops or latches)
- Latches are transparent, the output changes with the input if enabled
- Flip-flops are not transparent, the output only changes at on of the clock signal edges