Computer Electronics
Computer Electronics
Lecture 4: FPGAs

---
Outline
Outline
Programmable hardware
  - FPGAs
  - CGRAs
- Worksheet #4

---
Programmable Hardware
Programmable Hardware
- Designing hardware is challenging, expensive and error prone
- A re-spin of an IC can cost 100s of M$ in modern nodes (e.g. 22 nm)
- Is there a way to “program circuits” and fix them if there are errors or updates?
- YES: electrically programmable digital circuits!

---
Types of Programmable Hardware
Types of Programmable Hardware
Fine grain:
  - Field Programmable Logic Arrays (FPGAS)
- Coarse Grain:
  - Coarse Grained Reconfigurable Arrays (CGRAs)
- Mixed

---
FPGAs
FPGAs
- Can implement almost any digital circuit
- Useful in prototyping chips
- Useful in low volume products
  - 100s of K units and below
  - Beats IC unit costs!
- Clock frequencies well below ICs
- Cheap development cost
  - FPGA tools are cheap, design flow is relatively simple

---
FPGAs
FPGAs
Early 1980
  - Standard IC circuits (microprocessors, bus, I/O controllers, timers, …) had to be interconnected (serial/parallel, multiplexing, …)
  - Custom ICs were used for the interconnection logic but had huge cost and long development.
- 1984
  - Xilinx started selling FPGAs
  - Concept invented in 1967 by Wahlstrom
  - No physical layout, no mask making, no IC manufacturing, lower NRE costs and short time to market.

---
FPGA basic architecture
FPGA basic architecture

---
Basic Programmable Logic Block
Basic Programmable Logic Block

---
Basic slice
Basic slice

---
Real slice
Real slice

---
Look-Up Table (LUT)
Look-Up Table (LUT)
- Structure: memory
- Implementation: Latch+ Multiplexer (!cost)
LUT inputs
(memory address)
Configuration bits (memory contents)

---
Programmable IO
Programmable IO

---
Programmable interconnections
Programmable interconnections
Local CLB interconnection
Connection to neighbor CLBs
Connection to distant CLBs

---
Switch matrices
Switch matrices
A
B
0/1
Configuration bit:
0: A not connected to B
1: A connected to B

---
Interconnect line types
Interconnect line types
- Long Lines: bidirectional wires that distribute signals across the device. Vertical and horizontal long lines span the full height and width of the device.
- Hex Lines: route signals to every third or sixth block away in all four directions.
- Double Lines: route signals to every first or second block away in all four directions.
- Direct Lines: route signals to neighboring blocks—vertically, horizontally, and diagonally.
- Fast Lines: internal CLB local interconnections from LUT outputs to LUT inputs.

---
Configuration architecture
Configuration architecture
RAM organization
Address and configuration data
(bitstream)
Configuration bits/nibbles/bytes/words
Address decoder

---
Memory and arithmetic
Memory and arithmetic
- FPGAs can be programmed to implement registers, register files or larger memories
- FPGAs can be programmed to implement complex arithmetic units such as multipliers
- But, this consumes a lot of LUTS

---
Heterogenous FPGAs
Heterogenous FPGAs
- Contain embedded RAMs
- Contain embedded DSP blocks
  - Multiply Accumulate units (MACC) and variations
    - Multiply only
    - Add only, etc
- Result: better silicon utilization leads to lower price products

---
FPGA layout
FPGA layout

---
Worksheet 4
- An FPGA is 2x2 LUT2 matrix and has 4 IOs
- Each LUT input can select any FPGA primary input and any LUT output
- Each FPGA output can select any LUT output, registered or not
1. Draw the FPGA block diagram, showing its inputs and outputs, its LUTs, their programmable input selection muxes and the programmable input muxes of the FPGA outputs.
2. Indicate the state of the configuration bits to program 1-bit counter function in the above LUT.