Computer Electronics
Computer Electronics
Lecture 9: Multiplier Circuits – Part 1

---
Matrix multipliers: algorithm
Matrix multipliers: algorithm
multiplicand
multiplier
partial product0
partial product1
partial product2
partial product3
product

---
Matrix multiplier: notation
Matrix multiplier: notation

---
Matrix multiplier with ripple carry
Matrix multiplier with ripple carry

---
Pipelined MM w/ RCA
Pipelined MM w/ RCA
- Pipeline stages after each partial product addition
- What is the maximum clock frequency?

---
Carry-Save Adder Principle
Carry-Save Adder Principle
Ripple-carry
adder
Carry-save
Adder stage

---
3-input adder using carry-save stage
3-input adder using carry-save stage
Carry-save
Adder stage
Carry-save
based adder
Ripple-carry
adder

---
Matrix multiplier with carry save
Matrix multiplier with carry save

---
Pipelined MM w/ CSaA
Pipelined MM w/ CSaA
- Pipeline stages after each partial product addition
- What is the maximum clock frequency?
  - What is the stage responsible for it?
- Solution for increasing the frequency
  - Work at the CSaA clock frequency
  - Use N-1 clock cycles to compute the last stage

---
Worksheet #9
Design a 2-bit carry-save unsigned multiplier and simulate all possible 16 combinations of the inputs