Computer Electronics
Computer Electronics
Lecture 22: SRAM

---
Outline
Outline
- Static memory cells
- DRAM vs. SRAM
- SRAM read operation
- SRAM write operation
- SRAM sense and write amplifiers

---
A static memory cell
A static memory cell

---
Static cell types
Static cell types

---
Poly load
Poly load
- Implemented in a separate polysilicon layer
- Advantage:
  - 30% area reduction
- Disadvantages
  - Non standard technology
  - Resistors can’t be shrunk anymore

---
TFT PMOS
TFT PMOS
- Polysilicon transistor built on top of NMOS transistor
- Advantage:
  - Area reduction
- Disadvantage
  - Non standard technology

---
Loadless SRAM Cell
Loadless SRAM Cell
- Information stored in gate capacitor
- Advantages:
  - Standard technology
  - Up to 65% area reduction!
- Disadvantage
  - Leakage current may wipe info away

---
6T standard SRAM cell
6T standard SRAM cell
- Most common SRAM cell
- Advantage:
  - Implemented with regular CMOS technology
- Disadvantage
  - Larger area

---
SRAM write summary
SRAM vs DRAM
- Cells are much larger: 6T instead of 1T+1C(parasitic). DRAM is denser
- Cells consume only leakage current, no expensive periodic refresh. SRAM is lower power
- Cost is exponential with area due to Yield problems
- SRAM much more expensive than DRAM (cost per bit)

---
SRAM read operation
SRAM read operation

---
SRAM read circuit
VDD
- Pre-charge BL at VDD
- Turn on the access switch
- Wait for a voltage at BL to drop
- Note that BLB voltage stuck at VDD
- ID = k(VDD-VT)² (constant current discharge)
- Δ t = Cd ΔV / ID
Ideal switch
BL
VDD-ΔV
VDD

---
SRAM read procedure
1. Pre-charge BL and BLB at the same voltage VDD
2. Turn on the access transistors (row decoder)
3. Wait for a voltage difference to develop between BL and BLB
4. Select the column (column decoder) to access the (shared) sense amplifier and wait for voltage levels to be restored
5. Read the SRAM data IO pins

---
SRAM write operation
SRAM write operation

---
SRAM read summary
SRAM write circuit
VDD
- Pre-charge BLB at VDD
- Turn on the access switch (row)
- Apply write amp (column)
- BL discharges slowly via cell
- BLB discharges fast via write transistor
- Simple model: write transistor is resistor Ra, cell transistor too weak, ideal switch
‘0’
SRAM cell
pull-up
VDD
Ideal switch
BL
%DELTA t = R_A C_D ln ( V_{DD} over {V_{DD}/2} ) = R_A C_D ln ( 2 )
VDD→VDD/2
Initially stored ‘1’:
BL = ‘1’, BLB=’0’
Write ‘0’:
BL=’1’
BLB=’0’
VDD
X
Y
Δt = RC ln(X/Y)

---
SRAM write procedure
1. Pre-charge BL and BLB at VDD
2. Apply the write values to the chip IO pins
3. Select the row to provide an electrical access to the cell
4. Select the column so that the (shared) write amplifier will drive and force the cell to the desired state

---
Shared sense and write amps
Shared sense and write amps

---
SRAM write amplifier
SRAM write amplifier
- Use pre-charge facility already in place for reading
- Use simple pull-down transistors for writing
- If pre-charge value is VDD then only one line needs to be pulled down!