Computer Electronics
Computer Electronics
Lecture 3: The picoVersat Controller

---
Outline
Outline
- picoVersat architecture
- PicoVersat instruction set
- PicoVersat assembler
- Example program
- Assembling and running the program the Icarus Verilog simulator
- Worksheet #3

---
Example: the Versat Controller
The picoVersat Controller
- A really tiny controller processor (500 logic gates)
- Originally used to control the Versat CGRA (sort of FPGA)
- 16 instructions, accumulator machine

---
The picoVersat Instruction Format

---
The picoVersat HW Architecture

---
Versat Load/Store instructions
picoVersat Load/Store instructions
1. RDW: Load to RA (address as immediate)
2. WRW: Store from RA (address as immediate )
3. RDWB: Load to RA (address in RB)
4. WRWB: Store from RA (address in RB)
5. LDI: Load immediate to low part (27:0) of RA, sign extension in high part
6. LDIH: Load immediate to high part (31:16) of RA, keep low part (15:0)

---
Versat Arithmetic/Logical instructions
picoVersat Arithmetic/Logical instructions
1. AND: Logic AND with RA (address as immediate)
2. SHFT: Shift RA 1 bit to left/right (direction as immediate, arithmetic shift)
3. ADDI: Add immediate to RA
4. ADD: Add to RA (address as immediate)
5. SUB: Subtract from RA (address as immediate)

---
Versat branch instructions
Versat branch instructions
1. BEQI: Branch to immediate address if RA=0
2. BNEQI: Branch to immediate address if RA!=0
3. BEQ: Branch to address in RB if RA=0
4. BNEQ: Branch to pointer in RB if RA!=0

---
Exercise
- Write a picoversat program that
  - Computes c=a*b, where a and b are 2 integers resident in known memory positions
  - Prints the result using a nprt (number printer) peripheral similar to the cprt (char printer) peripheral in the hello_world example program