Computer Electronics
Computer Electronics
Lecture 17: Dynamic Random Access Memory (DRAM)

---
Outline
Outline
- DRAM cell
- DRAM matrix
- DRAM read
- DRAM write
- DRAM high-level operation
- DRAM module organization
- DRAM refresh
- Real DRAM chips

---
DRAM Cell
DRAM Cell

---
DRAM cell matrix
DRAM cell matrix

---
DRAM Reading  problem
DRAM Reading problem
- Select Row using address
- Cell charge has little effect on line voltage Vd because Cc << Cd
- Final voltage
- For Cc=40fF, Cd=1pF, Vc=5V then the variation in Vd is only 200mV
- Since the transistors leak current, then variation is even smaller
- Difficult to detect this small variation!
V = C_d over { C_c+C_d } V_d + C_c over { C_c+C_d } V_c
Cc
Cd

---
Solving the read problem
Charge redistribution
Switch closes at time t=0
Charge is conserved
S
Cd
Cc
Q( t = infinity ) = Q( t < 0) newline newline Q=CV newline newline C_d V_d + C_c V_c = (C_c+C_d)V( t = infinity )
V = C_d over { C_c+C_d } V_d + C_c over { C_c+C_d } V_c
Energy NOT conserved: part of it is dissipated in the switch S (resistance Rs)
E(t = infinity) = 1 over 2 ( C_d+C_c ) V^2(infinity) newline E(t = infinity) = 1 over 2 ( C_d+C_c ) ( C_d over { C_c+C_d } V_d + C_c over { C_c+C_d } V_c )^2 newline E(t = infinity) = 1 over 2 C_d^2 over { C_d+C_c} V_d^2 + {C_d C_c} over { C_d+C_c} V_d V_c + 1 over 2 C_c^2 over { C_d+C_c} V_c^2 newline newline E (t<0) > E(t = infinity)
E=1 over 2 C V^2 newline newline E(t < 0) = 1 over 2 C_d V_d^2 + 1 over 2 C_c V_c^2 newline
V(t) = V( infinity ) + [ VDD over 2 - V(infinity) ] e^{ -t over {R_s {C_d C_c} over (C_d + C_c)}}

---
Solving the read problem
- Use complementary column bit lines to store d and ~d (doubles circuit area, not necessary but eases explanation)
- Pre-charge the bit lines at Vdd/2
- Select row and cells will drive bit lines
Vd=Vdd/2+ΔV/2 and V~d=Vdd/2-ΔV/2
- Amplify ΔV using sense amp
- Select column to read data

---
Pre-charge complementary bit lines
Pre-charge complementary bit lines
d
~d
Vdd/2
Voltage equalization circuit
Pre-charge enable
(disable after complete)

---
Select row, sense and read
Select row, sense and read
d
~d
- Select row to drive bit lines
  Vd=Vdd/2+ΔV/2
  V~d=Vdd/2-ΔV/2
- Amplify ΔV using sense amp – This also restores the cells!
- Select column to read data
Select Row
Power Up
Sense Amp
Select Column

---
DRAM high-level view
DRAM high-level view
Example:
1024 x 1024 mem array
20 address bits
Only 10 address pins
Send row address
Then send column address

---
DRAM timing diagram
DRAM timing diagram

---
DRAM fast page mode
DRAM fast page mode

---
DRAM Extended Data Output (EDO)
DRAM Extended Data Output (EDO)
Uses register to hold previously read data while new data is read
Pipelined access!

---
Burst Extended Data Output (BEDO)
Burst Extended Data Output (BEDO)
Column address is incremented internally for greater speed!

---
Synchronous (SDRAM)
Synchronous (SDRAM)
Synchronous operation facilitates external generation of signals
Column address still incremented internally like BEDO

---
Double Data Rate (DDR)
Double Data Rate (DDR)
Like SDRAM but data made available at both clock edges
Bandwidth is doubled!

---
Configuring CPU to use some DRAM
Configuring CPU to use some DRAM
BASIC COMMANDS
Next row precharge
Activate row
Activate column
Read/Write data
tRP: precharge time new row
tRCD: RAS to CAS delay
tCL: CAS to data delay
tRAS = tRCD+2tCL
tRC = tRAS+tRP

---
Memory module organization
Memory module organization

---
Serial presence detect
Serial presence detect
- Modules have a small chip to inform whether they are present
- Useful in Power On Self Test (POST)

---
DRAM refreshing
DRAM refreshing
- Cell transistors leak and lose charge
- Cell needs refreshing before stored info is lost
- When a cell is read it is restored (refreshed)

---
DRAM refresh modes
DRAM refresh modes
- RAS only
- CAS before RAS
- Hidden

---
RAS only refresh
RAS only refresh
address
data
Provide Row address and activate RAS
No need to activate CAS

---
CAS before RAS refresh
CAS before RAS refresh
No need to provide Row address (incremented internally)
This is signaled by activating CAS before RAS

---
Hidden refresh
Hidden refresh
- Performs refresh while data is output
- Reduces refresh overhead

---
Refresh overhead
Refresh overhead
- Refresh interval: every row must be refreshed within this interval
- Refresh time: time to refresh all rows
- Overhead = refresh time/refresh interval