Computer Electronics
Computer Electronics
Lecture 4: FPGAs

---
Programmable Hardware
Programmable Hardware
- Designing hardware is challenging, expensive and error prone
- A re-spin of an IC can cost 100s of M$ in modern nodes (e.g. 22 nm)
- Is there a way to “program circuits” and fix them if there are errors or updates?
- YES: electrically programmable digital circuits!

---
FPGAs
Field Programmable Gate Array (FPGA)
- Can implement any digital circuit, if it fits in the device
- Useful in prototyping chips
- Traditionally useful in low production volume products
  - 100s of K units and below
  - Beats IC unit costs!
- Clock frequencies well below ICs
- Cheap development cost
  - FPGA tools are cheap, design flow is relatively simple
- Nowadays useful as a general purpose processor, with high production volumes, like GPUs!!

---
FPGAs
Early FPGA History
Early 1980
  - Standard IC circuits (microprocessors, bus, I/O controllers, timers, …) had to be interconnected (serial/parallel, multiplexing, …)
  - Custom ICs were used for the interconnection logic but had huge cost and long development.
- 1984
  - Xilinx started selling FPGAs
  - Concept invented in 1967 by Wahlstrom
  - No physical layout, no mask making, no IC manufacturing, lower NRE costs and short time to market.

---
FPGA basic architecture
FPGA basic architecture

---
Basic Programmable Logic Block
Basic Programmable Logic Block

---
Basic slice
Basic slice

---
Real slice
Real slice

---
Look-Up Table (LUT)
Look-Up Table (LUT)
- Structure: a very small memory
- Implementation: Latch + Multiplexer
LUT inputs
(memory address)
Configuration bits (memory contents)

---
Programmable IO
Programmable IO

---
Programmable interconnections
Programmable interconnections
Local CLB interconnection
Connection to neighbor CLBs
Connection to distant CLBs

---
Switch matrices
Switch matrices
A
B
0/1
Configuration bit:
0: A not connected to B
1: A connected to B

---
Interconnect line types
Interconnect line types
- Long Lines: bidirectional wires that distribute signals across the device. Vertical and horizontal long lines span the full height and width of the device.
- Hex Lines: route signals to every third or sixth block away in all four directions.
- Double Lines: route signals to every first or second block away in all four directions.
- Direct Lines: route signals to neighboring blocks—vertically, horizontally, and diagonally.
- Fast Lines: internal CLB local interconnections from LUT outputs to LUT inputs.

---
Configuration architecture
Configuration architecture
RAM organization
Address and configuration data
(bitstream)
Configuration bits/nibbles/bytes/words
Address decoder

---
Memory and arithmetic
Memory and arithmetic
- FPGAs can be programmed to implement registers, register files or larger memories
- The LUTs can be used to implement larger register files or small memories
- FPGAs can be programmed to implement complex arithmetic units such as multipliers
- But, this consumes a lot of LUTs

---
Heterogenous FPGAs
Heterogenous FPGAs
- Contain embedded RAMs
- Contain embedded DSP blocks
  - Multiply Accumulate units (MACC) and variations
    - Multiply only
    - Add only
    - Multiply an accumulate: mul + add
- Result: better silicon utilization leads to lower price products

---
FPGA layout
FPGA layout

---
Example FPGA
P0..3: pins, programmable with the following word:
Bit 3 – function select bit: input (0) or output (1)
Bits 2:1 – select which pin or LUT output
Bit 0 – selects FPGA pins (0) or LUT outputs (1);
L0..3: 2-input (A and B) LUTs, programmable with the following word:
Bits 9:6 – function select bits F(A,B)
Bits 5:3 – input B selection bits;
Bits 2:0 – input A selection bits;
P0
L0
L1
P3
P1
L3
L2
P2

---
Example FPGA
FPGA configuration (bitstream)
P0
L0
L1
PIN config
LUT2 config
P3
P1
L3
L2
P0
P1
P2
P3
L0
L1
L2
L3
P2
FUNCTION
IN
FUNCTION
INB
INA
1 + 3 = 4 4 + 3 + 3 = 10
Total configuration bits: 4*4 + 4*10 = 56 bits

---
Example FPGA
Configure logic function Y = X1 X2 X3
P0..2 are inputs
Config: 0 - - - (0 selects input function, since it is not an output the selection bits are don't care)
P3 is output:
Config: 1 10 1 (1 selects output function, 10 selects L2, 1 selects LUTs)
L0 and L1 are AND2:
L0 config: 1000 01 0 00 0 ( 1000 selects function AND, 01 0 selects P1 and 00 0 select P0 )
L1 config: 1000 10 0 00 1 (1000 selects function AND, 10 0 selects P2 and 00 1 selects L0 )
P0
L0
L1
P3
P1
L3
L2
P2
PIN X1
(P0)
A
AND2
(L0)
PIN X2
(P1)
AND2
(L1)
A
B
PIN Y
(P3)
B
PIN X3
(P2)