Computer Electronics
Computer Electronics
Lecture 13: FPGAs and CGRAs

---
Outline
Outline
Programmable hardware
  - FPGAs
  - CGRAs
- The Versat CGRA

---
Programmable Hardware
Programmable Hardware
- Designing hardware is challenging, expensive and error prone
- A re-spin of an IC can cost 100s of M$ in modern nodes (e.g. 22 nm)
- Is there a way to “program circuits” and fix them if there are errors or updates?
- YES: electrically programmable digital circuits!

---
Types of Programmable Hardware
Types of Programmable Hardware
Fine grain:
  - Field Programmable Logic Arrays (FPGAS)
- Coarse Grain:
  - Coarse Grained Reconfigurable Arrays (CGRAs)
- Mixed

---
FPGAs
FPGAs
- Can implement almost any digital circuit
- Useful in prototyping chips
- Useful in low volume products
  - 100s of K units and below
  - Beats IC unit costs!
- Clock frequencies well below ICs
- Cheap development cost
  - FPGA tools are cheap, design flow is relatively simple

---
FPGAs
FPGAs
Early 1980
  - Standard IC circuits (microprocessors, bus, I/O controllers, timers, …) had to be interconnected (serial/parallel, multiplexing, …)
  - Custom ICs were used for the interconnection logic but had huge cost and long development.
- 1984
  - Xilinx started selling FPGAs
  - Concept invented in 1967 by Wahlstrom
  - No physical layout, no mask making, no IC manufacturing, lower NRE costs and short time to market.

---
FPGA basic architecture
FPGA basic architecture

---
Basic Programmable Logic Block
Basic Programmable Logic Block

---
Basic slice
Basic slice

---
Real slice
Real slice

---
Look-Up Table (LUT)
Look-Up Table (LUT)
- Structure: memory
- Implementation: Latch+ Multiplexer (!cost)
LUT inputs
(memory address)
Configuration bits (memory contents)

---
Programmable IO
Programmable IO

---
Programmable interconnections
Programmable interconnections
Local CLB interconnection
Connection to neighbor CLBs
Connection to distant CLBs

---
Switch matrices
Switch matrices
A
B
0/1
Configuration bit:
0: A not connected to B
1: A connected to B

---
Interconnect line types
Interconnect line types
- Long Lines: bidirectional wires that distribute signals across the device. Vertical and horizontal long lines span the full height and width of the device.
- Hex Lines: route signals to every third or sixth block away in all four directions.
- Double Lines: route signals to every first or second block away in all four directions.
- Direct Lines: route signals to neighboring blocks—vertically, horizontally, and diagonally.
- Fast Lines: internal CLB local interconnections from LUT outputs to LUT inputs.

---
Configuration architecture
Configuration architecture
RAM organization
Address and configuration data
(bitstream)
Configuration bits/nibbles/bytes/words
Address decoder

---
Memory and arithmetic
Memory and arithmetic
- FPGAs can be programmed to implement registers, register files or larger memories
- FPGAs can be programmed to implement complex arithmetic units such as multipliers
- But, this consumes a lot of LUTS

---
Heterogenous FPGAs
Heterogenous FPGAs
- Contain embedded RAMs
- Contain embedded DSP blocks
  - Multiply Accumulate units (MACC) and variations
    - Multiply only
    - Add only, etc
- Result: better silicon utilization leads to lower price products

---
FPGA layout
FPGA layout