Computer Electronics
Computer Electronics
Lecture 18: Multiplier Circuits – Part 1

---
Lecture outline
Lecture outline
- Parallel unsigned multiplier
- Parallel carry-save multiplier
- Signed multiplier
  - Subtraction review
  - Parallel signed multiplier

---
Matrix multiplier: notation
Unigned matrix multiplier: algorithm
multiplicand
a3 a2 a1 a0
x b3 b2 b1 b0
a3b0 a2b0 a1b0 a0b0
a3b1 a2b1 a1b1 a0b1
a3b2 a2b2 a1b2 a0b2
 + a3b3 a2b3 a1b3 a0b3
p7 p6 p5 p4 p3 p2 p1 p0
multiplier
partial product
product

---
Matrix multiplier with ripple carry
Matrix multiplier with ripple carry
cd
ab

---
Pipelined MM w/ RCA
Pipelined MM w/ RCA
- Pipeline stages after each partial product addition
- What is the maximum clock frequency?

---
Carry-Save Adder Principle
Carry-Save Adder Principle
Ripple-carry
adder
Carry-save
Adder stage

---
3-input adder using carry-save stage
3-input adder using carry-save stage
Carry-save
Adder stage
Carry-save
based adder
Ripple-carry
adder

---
Matrix multiplier with carry save
Matrix multiplier with carry save

---
Pipelined MM w/ CSaA
Pipelined MM w/ CSaA
- Pipeline stages after each partial product addition
- What is the maximum clock frequency?
  - What is the stage responsible for it?
- Solution for increasing the frequency
  - Work at the CSaA clock frequency
  - Use N-1 clock cycles to compute the last stage

---
Subtraction: fundamentals
Subtraction: fundamentals
- Adder circuits work equally well with unsigned and signed numbers
- A-B = A + (-B)
  - To subtract simply add the symmetric
  - Symmetric is 2’s complement
  - Easiest way to compute 2’s complement in hardware
    - Complement and add 1

---
Subtraction: circuit
Subtraction: circuit

---
Sign extension
Sign extension
- Sometimes we need to increase the number of bits for representation in different signed integer format
- Sign of the number should be preserved
- Q1: represent signed number 1000 (-810) with 8 bits
- A1: 11111000 (sign extension in red)
- Q2: represent signed number 0111 (710) with 8 bits
- A2: 00000111(sign extension in red)

---
Logical/Arithmetic right shift
Logical/Arithmetic right shift
- Shifting a number left by p positions is the same as multiplying it by 2p
- Shifting a signed number right by p positions is the same as dividing it by 2p
- Sign must me preserved: arithmetic right shift
- 1000 (-810) shift right by 2 (divide by 4)
  - Logical right shift 0010 (210): wrong!
  - Arithmetic right shift 1110 (-210): correct!

---
Signed multiplication: fundamentals
Signed multiplication: fundamentals
- A = a3 a2 a1 a0, B = b3 b2 b1 b0
- In decimal notation
B = -b3*23 + b2*22 + b1*21 + b0*20
A*B = A * [-b3*23+ b2*22 + b1*21 + b0*20]
Algorithm:
  - Add least significant partial products, subtract most significant partial product

---
Signed multiplication: circuit
1
Signed multiplication: circuit
a3b0
a2b0
a1b0
a0b0
a3b1
a3b1
a2b1
a1b1
a0b1
FA
FA
FA
HA
FA
FA’
a3b2
a3b2
a2b2
a1b2
a0b2
FA
FA
FA
HA
FA’
a3b3
a3b3
a2b3
a1b3
a0b3
FA
FA
FA
FA
FA’
1
p7
p6
p5
p4
p3
p2
p1
p0