Computer Electronics
Computer Electronics
Lecture 24: Cache

---
Outline
Outline
- Motivation
- The cache concept
- Memory address structure for using cache
- Directly mapped cache
- Fully associative cache
- K-way associative cache
- Replacement policy
- Write policies

---
Motivation
Motivation
- Accessing main memory (off-chip DRAM) is slow due to latency of memory controller and memory itself
- The cache is a smaller SRAM on-chip memory that can be accessed in 1 clock cycle preferably
- Typical cache sizes are in the order of tens of kB
- Instructions or data word (32 or 64 bits) accessed using a parallel bus
- Look at iob-cache

---
The Cache concept
The Cache Concept
Memory (DRAM)
CPU
Cache
Disk
Small and fast
Very large and slow
Large and slow
Cache may have multiple levels successively slower but larger: L1, L2, L3… 2 or 3 levels common
Definitions
p: cache hit rate
1-p: cache miss rate
Tc: cache access time
Tm: memory access time (miss penalty)
Ta: average access time
Principle of Locality
In space: data in near addresses are more likely to be accessed
In time: data recently accessed is more likely to be accessed again
Ta = pTc+(1-p)Tm

---
Cache organization
Memory address structure for using cache
Main memory is divided into N address sets
Each set element stores Y ways of L data lines
Each data line has W words
Each word has B bytes
Byte offset : select byte in word
Structure of a main memory address (char *addr)
Byte Offset
Word Offset
Tag
Set ID
log2(N) bits
log2(B) bits
log2(W) bits
ADDR_W
Tag bits = ADDR_W-log2(N*W*B) bits

---
Memory address example
1GB memory: 32 sets, 4 ways, 4B words, 8 data words/line
1GB → 30 address bits ( log2(2³⁰) )
32 sets → 5 set ID bits ( log2(32) )
Cache size = 32 sets * 4 ways * 8 words/line * 4 bytes/word = exp2(5+2+3+2) = 4kB
Word Offset + Byte Offset
Tag
Set ID
5 bits
3+2 bits
30-5-5= 20 bits
ADDR_W = 30

---
Number of bits
Number of bits in the address
- #byte offset bits = log2(#bytes per word)
- #word offset bits = log2(#words per line)
- #set index bits = log2(#sets)
- #tag bits = #address bits – #byte offset bits - #word offset bits - #set index bits

---
Set visualization
Main memory (each color is a set)
1GB memory, 4 sets, 4 byte data words
1GB → 30 address bits ( log2(2³⁰) )
4 sets → 2 set ID bits ( log2(4) )
addresses 0:3 (set 0, tag 0)
addresses 7:4 (set 1, tag 0)
addresses 11:8 (set 2, tag 0)
addresses 15:12 (set 3, tag 0)
addresses 19:16 (set 0, tag 1)
addresses 23:20 (set 1, tag 1)
addresses 27:24 (set 2, tag 1)
addresses 31:28 (set 3, tag 1)
Etc.

---
Directly Mapped Cache
(each set only has 1 line in cache)
Directly Mapped Cache
1-way cache
Each set only has 1 line in cache
Each line has L data words
Memory address
Tag	Line
	WL-1, WL-2, …, W1, W0
Offset
Tag
Set
Set 1
Addressed set
Set n
==
Data word
HIT / MISS

---
Fully Associative Cache
(single set, multiple lines)
Fully Associative Cache
(single set, multiple lines)
Memory address
Tag
Line
Tag
Line
…
Tag
Offset
==
==
Encoder
HIT / MISS
Selected line
Data word

---
K-Way Set Associative Cache
(each set has k lines in cache)
K-Way Set Associative Cache
(each set has k lines in cache)
Memory address
Tag k-1	Line k-1	…	Tag 0	Line 0
Offset
Tag
Set
==?
==?
Line Select
Word Select
Encoder
Data Word
HIT / MISS

---
Cache replacement policy
Cache line replacement policy
- Upon a cache miss, line must be replaced
- Directly mapped cache (aka 1-way cache)
  - Only one line to choose – no choice
- K-way cache replacement policy
  - Random replace (RR): needs random counter – easy
  - Least recently used (LRU): needs usage record – difficult
  - Pseudo LRU: needs 1 bit for the last used, replace adjacent – easy
  - Most recently used (MRU): needs 1 bit for the last used – easy
  - Least Frequently Used: needs frequency counter – difficult
  - …. 17 policies listed in Wikipedia…

---
Cache write policy
Cache write policy
Write-through
  - data word (not block) is written to cache and main memory in case of a hit (miss case analyzed separately)
- Write-back
  - Data is written to cache only in case of a hit (miss case analyzed separately)
  - Data is written to memory only when line is replaced
  - Performance improvement with Dirty bit
    - Dirty bit is set when line is modified
    - Upon replacement, data is saved in memory only if Dirty bit is set

---
Write through hardware
Write through hardware
Cache
Memory
CPU
Write-Through buffer

---
Write-through buffer overflow
Write-through buffer overflow
Memory
Cache L2
CPU
Cache L1
Write-through buffer (FIFO)
Problem: If write frequency greater than word write time to memory than WTB becomes full
Solution: use 2 cache levels, as writing to L2 cache is faster than writing to memory

---
Cache write miss policy
Cache write miss policy
- What to do when line to write is not in cache
- Write Allocate policy
  - Transfer line to cache (allocate), then write to it
- Write Not-Allocate
  - Write to main memory only
- Usual policy combination
  - Write-Through + Write Not-Allocate
  - Write-back + Write Allocate