Computer Electronics
Computer Electronics
Lecture 9: Digital Circuits and Verilog IV
Finite State Machines

---
Create circuits with iob-lib
- By combining iob-lib modules and macros, one can create many basic digital circuits
- Using the `IOB_VAR to compute signal values in `IOB_COMB, gives the user the true meaning of the Verilog ‘reg’ type and the ‘always @*’ statement
  - ‘reg’ is a data type to hold the result a of computation; it does not necessarily represent a physical wire and it NEVER represents a register despite its unfortunate name.

---
Finite State Machines
- Finite State Machines (FSMs) should be created when it is not obvious how to make the circuit with the basic iob-lib components
- An FSM is basically an `IOB_COMB block connected to an `IOB_REG block
Inputs
`IOB_COMB
Outputs
`IOB_REG
Current state
Next state

---
FSM Types: Moore and Mealy
- Moore: Outputs = F(Current State)
  - Advantages:
    - Critical path does not include inputs so one has better control on timing closure
    - One state / one output is sometimes easier to design
  - Disadvantages
    - May need a few state transitions (1 clock cycle each) to produce the right output: slower reaction
    - More states = more logic: more registers, more state decoding combinatorial circuits
- Mealy: Outputs = F(Inputs, Current State)
  - Advantages:
    - Fewer states = less logic: less registers, less state decoding combinatorial circuits
    - Needs less state transitions (1 clock cycle each) to produce the right output: faster reaction
  - Disadvantages
    - critical path includes inputs so one has worse control on timing closure
    - One state multiple possible outputs is sometimes more difficult to design

---
Example: counting cars in a parking lot
Outputs: {acc_en, acc_in}
`IOB_ACC_ARE
car_count
Inputs: {car_in, car_out}
`IOB_COMB
Current state
This FSM controls an accumulator with enable to count the cars
Next state
`IOB_REG

---
Moore implementation: state transition diagram
car_out
Output decoding
State	acc_en	acc_in
idle	0	0
incr	1	1
decr	1	-1
Both 0 or both 1
Idle
decr
Both 0 or both 1
incr
car_out
car_in
car_in
Both 0 or both 1
Since the outputs (accumulator inputs) must be given by a state, we need three: idle, incr (increment the accumulator) and decr (decrement it)

---
   Moore implementation: state encoding and next state decoder
state[1]	state[0]	car_in	car_out	state_next[1]	state_next[0]
0	0	0	0	0	0
0	0	0	1	1	1
0	0	1	0	0	1
0	0	1	1	0	0
0	1	0	0	0	0
0	1	0	1	1	1
0	1	1	0	0	1
0	1	1	1	0	0
1	0	0	0	-	-
1	0	0	1	-	-
1	0	1	0	-	-
1	0	1	1	-	-
1	1	0	0	0	0
1	1	0	1	1	1
1	1	1	0	0	1
1	1	1	1	0	0
State encoding (binary, one-hot,
…, or custom as below, for
convenience
name	state[1]	state[0]
idle	0	0
incr	0	1
decr	1	1
Illegal	1	0
assign acc_en = |state;
(note that |state= state[0] | state[1])
assign acc_in = state;

---
Moore: conclusions
- Needs 3 states
- State encoding done manually and conveniently
- Output decode logic avoided as outputs can be derived from state bits using trivial logic
- Next state decoding needs logic synthesis using:
  - Boolean algebra
  - Quine-McCluskey method
  - Karnaugh maps, etc
- Logic synthesis tools can do it very well from the Verilog code

---
Moore: Verilog
module moore (
  `IOB_INPUT(car_in, 1), `IOB_INPUT( car_out, 1),
  `IOB_OUTPUT( acc_en, 1), `IOB_OUTPUT(acc_in, 2),
);
`IOB_VAR(state, 2)
`IOB_VAR(state_nxt, 2)
localparam idle=0, incr=1, decr=3;
`IOB_COMB begin
state_nxt = state; //default assignment
case(state)
idle:
if(car_in & ~car_out)
state_nxt = incr;
else if(~car_in & car_out)
state_nxt = decr
incr:
if(~car_in & car_out)
state_nxt = decr
else if(car_in ^car_out)
state_nxt = idle;
decr:
if(car_in & ~car_out)
state_nxt = incr
else if(car_in ^ car_out)
state_nxt = idle;
default: //in principle this state is never reach
state_nxt = idle;
endcase
assign acc_en = (state == incr) || (state == decr);
assign acc_in[0] =state[0];
assign acc_in[1] = state[1];
endmodule

---
Mealy implementation: state transition diagram
Both 0 or both 1
car_in	car_out	acc_en	acc_in
0	0	0	00
0	1	1	11 (-1)
1	0	1	01 (+1)
1	1	0	00
s0
car_in
car_out
assign acc_en = car_in^car_out;
assign acc_in[0] =acc_en;
Assign acc_in[1] = acc_en & car_out;
A single state means we need $clog2(1)=0 bits to represent the state, i.e., we do not need any states.
We need only the output decoding logic as a function of the inputs

---
Mealy: conclusions
- For this example, the Mealy formulation leads to zero states because outputs can be a function of the inputs only
- In general, Mealy machines require less states than Moore’s, not always zero states as in this example
- In general, the output decode logic is more complex than Moore’s because the logic functions have more inputs; in this example, the output decode logic is trivial but this is not always the case
- Like Moore’s, the next state and output decoding need logic synthesis using:
  - Boolean algebra
  - Quinn-mcluskey method
  - Karnough maps, etc
- Logic synthesis tools can do it very well from the Verilog code

---
Mealy: Verilog implementation
//Mealy formulation requires zero states in this case
module mealy (
  input car_in,
  input car_out,
  output acc_en,
  output [1:0] acc_in
);
assign acc_en = car_in^car_out;
assign acc_in[0] =acc_en;
assign acc_in[1] = acc_en & car_out;
endmodule