Computer Electronics
Computer Electronics
Lecture 18: SRAM

---
Outline
Outline
- Static memory cells
- SRAM read operation
- SRAM write operation
- SRAM sense and write amplifiers
- Worksheet 18

---
A static memory cell
A static memory cell

---
Static cell types
Static cell types

---
Poly load
Poly load
- Implemented in a separate polysilicon layer
- Advantage:
  - 30% area reduction
- Disadvantages
  - Non standard technology
  - Resistors can’t be shrunk anymore

---
TFT PMOS
TFT PMOS
- Polysilicon transistor built on top of NMOS transistor
- Advantage:
  - Area reduction
- Disadvantage
  - Non standard technology

---
Loadless SRAM Cell
Loadless SRAM Cell
- Information stored in gate capacitor
- Advantages:
  - Standard technology
  - Up to 65% area reduction!
- Disadvantage
  - Leakage current may wipe away info

---
6T standard SRAM cell
6T standard SRAM cell
- Most common SRAM cell
- Advantage:
  - Implemented with regular CMOS technology
- Disadvantage
  - Larger area

---
SRAM read operation
SRAM read operation

---
SRAM read summary
SRAM read summary
1. Pre-charge BL and BLB at the same voltage: VDD, VDD/2 or other
2. Turn on the access transistors (WL decoder)
3. Wait for a voltage difference to develop between BL and BLB
4. Select the column (CL decoder)
5. Turn on the (column shared) sense amplifier and wait for voltage levels to be restored
6. Read the SRAM data IO pins

---
SRAM write operation
SRAM write operation

---
SRAM write summary
SRAM write summary
1. Pre-charge BL and BLB
2. Apply the write values to the chip IO pins
3. Select the column (CL decoder) and row (WL decoder) so that the write amp will force the cell to the desired state

---
Shared sense and write amps
Shared sense and write amps

---
SRAM write amplifier
SRAM write amplifier
- Use simple pull-down transistors
- If pre-charge value is VDD then only one line needs to be pulled down!

---
Youtube video
Youtube video
- CMOS SRAM lecture
- By Prof. Amitava Dasgupta (IIT, Madras)
- https://www.youtube.com/watch?v=KrqyvpU9Cu0

---
Worksheet #18
Worksheet #19
- Design the pre-charge circuit
- Design the sense amplifier
- Compute the read access time if
  - For WL, RC=1ns and tRISE or tFALL is defined for 90% of final value
  - For BL and BLB, ΔV/Δt=1V/ns
  - Pre-charge value is VDD*2/3, VDD=3.3V
  - Sense amp is turned on when ΔV=100mV and responds in 20ps.