Computer Electronics
Computer Electronics
Lecture 7: Digital Circuits and Verilog II

---
The FLIP-FLOP!
- Only D type is studied
- Verilog description is directly mapped to a library component
- Set (S) and Reset (R) are optional
- It is rare that S and R are simultaneously supported: no library component
- Responds to the rising (positive) edge of the clock (CLK)
- Responds to the falling (negative) edge of the clock if an inverter is placed at the CLK input (DANGER ZONE!)
- The optional Enable signal (EN) determines whether the flip-flop will respond or not to the clock edge
EN
CLK

---
Recap: any digital circuit
Inputs
`IOB_COMB
Outputs
iob_reg
Current state
Next state

---
Signal wires
- Circuits are blocks connected by wires that carry digital signals (0 or 1)
- So we need to declare and use wires
- Verilog describes two types of wires:
  - Type wire: used for connections and assign statements
  - Type reg: user for operation results within always and initial processes
- Using IOb Verilog macros:
  - Type wire: `IOB_WIRE(NAME, WIDTH)
  - Type reg: `IOB_VAR(NAME, WIDTH)

---
IOb-lib: making digital
hardware design easier
- https://github.com/IObundle/iob-lib
- The iob-lib repo contains
  - Useful Verilog macros to avoid writing the same Verilog description over and over again
  - Useful components (modules) to avoid writing the same Verilog description over and over again
- Enjoy!

---
IOb-lib: input and output ports
To declare a module:
module my_module
(
  `INPUT(X,8), //declare 8-bit input
  `INPUT(Y,8),
  `OUTPUT(Z,16) //declare 16-bit output
  `INOUT(F,32) //declare 32-bit bidirectional port
);
   <body of module>
endmodule

---
IOb-lib: instantiate components
To instantiate a component is same as in Verilog:
module my_system
(
`OUTPUT( C),
 //interface signals
);
   <body verilog code: preamble>
   my_module comp0 //component instance
   (
      .X(A), //component port
      .Y(B),
      .Z ( C), //is output
      .F (D)
  )
   <body verilog code: trailer>
endmodule
my_system
comp0
my_module
A
B
X
Y
Z
C

---
IOb-lib: signals
- To declare a signal:
  `SIGNAL(my_wonder_signal, 10)
- With normal Verilog it would be
- wire [9:0] my_wonder_signal;
- reg [9:0] my_wonder_signal;
- wire [0:9] my_wonder_signal;
- Etc...

---
IOb-lib: signed signals
- To declare a signed signal:
  `SIGNAL_SIGNED(my_wonder_signal, 10)
- With normal Verilog it would be
- wire signed [9:0] my_wonder_signal;
- reg signed [9:0] my_wonder_signal;
- wire signed [0:9] my_wonder_signal;
- Etc...

---
IOb-lib: special signals that can be used as outputs
- To get around the complexities of Verilog a special signal type is created in iob-lib:
  `SIGNAL_OUT(my_special_signal, 10)
- Used to connect to component outputs
- Connecting a `SIGNAL to a component output is an ERROR
- Cannot be used as the result of computations (to be explained)
- Using `SIGNAL_OUT as the result of a computation is an ERROR
- With normal Verilog it would be
  - You don’t want to know!!

---
IOb-lib: using `SIGNAL_OUT
module my_system
(
 //interface signals
//`OUTPUT(C,16) is also an alternative
);
   <body verilog code: preamble>
   `SIGNAL_OUT(C,16) //`SIGNAL(C,16) is an ERROR)
   my_module comp0 //component instance
   (
      .X(A), //component port
      .Y(B),
      .Z(C)
  )
   <body verilog code: trailer>
endmodule
my_system
comp0
A
B
X
Y
Z
C

---
IOb-lib: flip-flops
Flip-flop: stores 1 bit
`SIGNAL(D,1) //declare input signal D
`SIGNAL(Q,1) //declare output signal Q
`REG(clk, Q, D) //instantiate one flip-flop

---
IOb-lib: registers!
Inputs
Combinatorial circuit
Outputs
Register
Current state
Next state

---
IOb-lib: registers
Register: stores W bits
`SIGNAL(D,10) //declare input signal vector D
`SIGNAL(Q,10) //declare output signal vector Q
`REG(clk, Q, D) //instantiate register or flip-flop //array

---
IOb-lib: combinatorial circuits
Inputs
Combinatorial circuit
Outputs
Register
Current state
Next state

---
IOb-lib: combinatorial blocks
module my_system
(
 //interface signals
);
...
   `SIGNAL(z,10);
   `SIGNAL(y,10);
   `COMB begin
       //insert C-like expressions here: examples
       z = s? X: Y;
       y = a*(b+c);
       //IMPORTANT: z and y MUST be of type `SIGNAL: type `OUTPUT or `SIGNAL_OUT are ERROR!!!
   end
...
endmodule

---
IOb-lib: combinatorial block result to output problem
- So how to assign an output to the output of a combinatorial circuit?
- Answer: use signal to output conversion function
module my_system
(
`OUTPUT(Z, 10);
 //other interface signals
);
…
   `SIGNAL(z,10)
   `COMB begin
       ...
       z = s? X: Y;
       ...
   end
`SIGNAL2OUT(Z,z)
…
endmodule

---
IOb-lib: order of statements
In Verilog the order of statements is irrelevant since we are describing things, not procedures!
Signal declarations must precede their use
Inside a combinatorial block order is important because it is described procedurally
Only the result of the combinatorial block matters and this may be affected by order
module my_system
(
 //interface signals
);
...
   `SIGNAL(z,10); //important to keep here
   `SIGNAL(y,10);
   `SIGNAL2OUT(Z,z) //not important to keep here
   `COMB begin
       //insert C-like expressions here: examples
       z = s? X: Y;
       y = a*(b+c);
       //IMPORTANT: z and y MUST be of type `SIGNAL: type `OUTPUT or `SIGNAL_OUT are ERROR!!!
   end
   //`SIGNAL2OUT(Z,z) //could be here...
endmodule