Computer Electronics
Computer Electronics
Lecture 4: IOb-SoC Tour (continued) and first Verilog notions

---
IOb-SoC: recap of last lesson & more
Dual-Port
I/D
Memory
CPU
Wrapper
I/D
IBUS
DBUS
PBUS
ACCELERATOR BUS
UART BUS
User
Hardware
Accelerator
UART
[Speaker Notes: Let’s simplify the vNA.]

---
IOb-SoC: directories
- Software: C/C++ software programs + python scripts for automation
- Hardware: verilog hardware descriptions
- Document: latex documents
- Submodules: other repositories used by Iob-SoC, uses git submodule technology

---
IOb-SoC: the software directory
- Directories
  - firmware: the program to run on IOb-SoC (modify to create your own program)
  - Do not edit these:
    - bootloader: the resident bootloader program
    - console: the PC program that communicates with the board
    - python: directory of build automation scripts
- Files: (not intended to be edited)
  - software.mk: makefile segment for software makefiles
  - system.h: system parameters extracted from configurations entered in .mk files
  - template.lds: linker script

---
Iob-SoC: linker script
SECTIONS {
        .memory : {
        . = 0x000000;
        *(.init);
        *(.text);
        *(*);
        . = ALIGN(4);
        _heap_start = .;
        end = .;
        }
}
.init
(this code section is declared
in the code itself)
.text
(all other unidentified code sections)
Statically allocated data
(global and local static variables)
Dynamically
allocated data
Also the initial Stack Pointer Value

---
IOb-SoC: the firmware directory
- Files (visit & understand)
  - Makefile: firmware top build script
    - Includes software.mk
  - firmware.S: the assembly start file
    - Includes system.h
  - firmware.c: the firmware C program
    - Includes system.h

---
Iob-SoC: bootloader, console, python
- Bootloader
  - Same structure as firmware
    - it is a normal program but used to boot the system
- Console
  - Compiled and run on the PC using normal gcc
  - Communicates with the target board where Iob-SoC is running via USB(TX)→RS232 (UART) → USB(RX)
  - (Sends the firmware to target and) commands it to run
  - May be run repeatedly during debug
- Python:
  - Contains scripts that are too cumbersome to do with Make commands or bash commands in the Make recipes

---
IOb-SoC: the hardware directory
- Directories (not intended to be edited)
  - src: the basic system verilog files
  - testbench: Verilog testbench
  - include: the Verilog header files (shared by many files)
  - simulation: build and run directories
  - fpga: build and run directories
  - asic: build and run directories
- Files: (not intended to be edited)
  - hardware.mk: makefile segment for hardware makefiles (simulation, fpga and asic)

---
IOb-SoC: the hardware/src directory
- Contains Verilog modules
- Verilog is a hardware DESCRIPTION language
- Verilog is not a programming language
- We are describing circuits not procedures
- We use procedures to describe circuits

---
Testbench and Unit Under Test (UUT)
Verilog module (a digital circuit)
Inputs
Verilog module
A Digital Circuit
Outputs
Inouts (bidirectional wires)

---
Verilog module (a circuit)
module my_unimaginable_peripheral
   (
    input clk,
    input rst,
    // native bus
    input valid,
    input [`SRAM_ADDR_W-3:0] addr,
    input [`DATA_W-1:0] wdata, //used for booting
    input [`DATA_W/8-1:0] wstrb, //used for booting
    output [`DATA_W-1:0] rdata,
    output ready
);
//description of module goes here
endmodule

---
The testbench directory
The testbench
Output
Signal analyzers
Input
UUT
Pass/Fail
Signal sources

---
Verilog testbench
(not a real circuit!)
Used in Verilog simulation!
module my_megapower_testbench;
//description of test hardware
//instance of the Unit Under Test
endmodule

---
Verilog header files
`include “my_humble_header_file.vh”
// this like the C language #include
module my_megapower_testbench;
//description of test hardware
//instance of the Unit Under Test
endmodule

---
IOb-SoC: the simulation directory
- Contains simulation build and run directories, one directory per simulator
  - Only the icarus simulator will be used
    - The icarus directory only has a simulation makefile (visit)
- Files:
  - the simulation.mk makefile segment (visit)
  - The waves.gtkw input file for the gtkwave program

---
IOb-SoC: the document directory
- Contains document build directories, one directory per document type
  - pb: product brief
    - Makefile
    - .tex files
    - .pdf file for easy viewing
    - Private figures directory
  - presentation: slide presentation
- Contains the figures directory
  - Figures that are shared among different documents

---
IOb-SoC: the submodules directory
- System submodules
  - CPU
  - CACHE
  - UART
- A git submodule is a pointer to another git repository
  - Allows for modular and distributed development :-)
  - Easy to add with the git submodule add <url> path/to/the/submodule :-)
  - Not so easy to remove: git submodule remove does not exist :-(
- The way the system collects hardware and software components from the submodules and assembles them in the system is the topic of the next class.