Computer Electronics
Computer Electronics
Lecture 3: Design Choices

---
How to choose a processor
How to choose a processor
- Several factors need to be accounted for
- In the end, the envisaged application will dictate the choice
- In many cases, a general purpose processor (GPP) available in the market is chosen

---
Advantages of selecting a GPP
Advantages of selecting a GPP
- Low NRE cost
- Short development time
- Great flexibility
- Low unitary cost
- Good performance for common tasks

---
Disadvantages of selecting a GPP
Disadvantages of selecting a GPP
- Low performance for some applications
- May be bigger than needed
- May consume more than can be afforded

---
ASSPs
ASSPs
- When GPPs are unsuitable, Application Specific Standard Products (ASSPs) are good solution
- An ASSP is an integrated circuit specific for a wide market applications (eg.: video coding)
- Cost is low since production volume is high and performance for that particular application

---
DSPs, GPUs
DSPs, GPUs
- In some cases your application can run well using a Digital Signal Processor (eg.: widely used for audio apps)
- In other cases GPUs can do it: many AI algorithms now use GPUs

---
FPGAs and ASICs
FPGAs and ASICs
- If you can’t find any suitable processor…
- An FPGA may be useful but cost is high, clock frequency is low, power is high, …
- In some cases only an Application Specific Integrated Circuit (ASIC) can be used…
- Possible strategy: prototype in FPGA, release as hybrid and finally make ASIC
- Xilinx EasyPath program: create an ASIC/FPGA hybrid

---
Microcontrollers (mCs)
Microcontrollers (mCs)
- Target control applications
- Have analog I/Os (internal ADCs and DACs)
- Have digital I/Os: RS232, USB, I2C, SPI and CAN.
- Using a mC avoids developing hardware for the above interfaces

---
Dedicated processors as ASICs
Dedicated processors as ASICs
- Developed from scratch: high NRE
- Function is well defined
- Cannot be changed after fabrication
  - Make sure to embed some configurability and programmability to reduce risk
- Market must be big to amortize NRE
- Reward: optimal performance, area and power consumption

---
Development stages
Development stages
- Top-down development (sometimes bottom-up)
- Top-level described in natural language, drawings, pseudo-code, etc
- Refine description to target GPPs or dedicated processors: behavioral descriptions
- Code for GPPs, RTL and code for dedicated
- Compile, synthesize: get machine code, netlist

---
Design technology
Design technology

---
Focus high-level, automate low-level
Focus high-level, automate low-level
- Create RTL descriptions using Verilog/VHDL
- Or use high-level synthesis
  - From High-level languages (eg. C++) to RTL automatically
- Write programs (Java/C++/python)
  - Compile for machine code
- Productivity:
  - Use software libraries and silicon IP – don’t reinvent the wheel

---
Specification
Specification
- Analyze needed functionalities using market and designer input and create set of specs
- Customers always want everything, now and for free
- Never ask customers what the product should be
- Ask them what will they use it for and check their background
- The designer will then elaborate a realistic set of specs

---
The specs
The specs
- Ordered by importance
- Compatible with all product features
- Non conflicting
- Unambiguous

---
Choice of components
Choice of components
- Make vs. buy decisions
- Do not waste time with optimal decisions
- Dedicated logic circuits are not always faster than existing processors
  - They may be smaller and cooler though
  - Or not at all
- Commercial processors very optimized
  - Thousands of person-years

---
The programmable advantage
The programmable advantage
- A multi-function circuit needs modules for each function
  - Functions can be done in parallel
- A processor uses the same hardware for multiple functions
  - Functions are done sequentially
- Trade-off performance for price/size/power

---
Difficulties
Difficulties
- A small team under tight deadlines has no time for detailed optimizations
- Big companies buy new interesting technologies from startups and optimize them over time (or just trash them)
- They only buy techs or invest in-house developing if price/NRE can be amortized or to get rid of competition

---
Hardware/software co-design
Hardware/software co-design
- Today chips are complex (SoCs)
- SoCs employ a number of standard processors and custom hardware
- Hardware and software development can happen in parallel
- SW can be tested before having HW by using simulators and emulators

---
Energy consumption
Energy consumption
- Light and portable? Need battery/solar
- Low energy consumption becomes hot feature: no frequent recharging!
- Remote locations: recharging awkward if not impossible

---
How to reduce energy consumption
How to reduce energy consumption
- Choose low power/energy components
- Power management algorithms to switch on/off parts of the circuit
- Choose suitable clock frequencies
  - Common to have multiple clock domains

---
EU environmental compliance directives
EU environmental compliance directives
- Directive 2002/95 / EC, known as RoHS (Restriction of Certain Hazardous Substances), prohibits the use of cadmium, mercury, hexavalent chromium, polybrominated biphenyls, diphenyl polybrominated ethers and lead.
- Directive 2002/96 / EC, known as WEEE (Waste from Electrical and Electronic Equipment), on the other hand, gives manufacturers responsibility for the reuse or destruction of discarded electrical and electronic products.

---
User interface (UI)
User interface (UI)
Some embedded systems barely need a UI
  - Internal processors and complex circuits get unnoticed by user
- Other systems require a complex UI
  - Often, the most complex part in the system
  - Developed by engineers, psychologists, designers, etc

---
UI importance
UI importance
- Engineers: any UI as long as I can do what I want with the device
- General public: no clue what’s inside
  - UI should reflect their intention
- Very powerful products with only few users
- Technically poor products with zillion users
- Appearance and perception as important as technical features

---
Documentation
Documentation
- Can’t figure it out? Check the doc
- Bad practice: build the whole system then write docs – details missed
- Good practice: document (and test) each submodule ASAP
- Use documents of submodules to produce top-level doc

---
Documents for engineers
Documents for engineers
- For team members
- For a substitute engineer
- For future engineers
- Time invested in docs returns in the form of:
  - Time saved recreating existing things
  - Time saved figuring out what it does

---
Document types for engineers
Document types for engineers
- Spec sheets
- Schematics
- Memos
  - Also README files and code comments
- Datasheets (also for users)
- User manuals (also for users)

---
Documents for users
Documents for users
- Good products can be killed by bad docs
- No bad products saved by good docs
- Types
  - Product briefs
  - Presentations (textual, slides, video)
  - Datasheets
  - Installation manuals
  - User manuals
  - Repair manuals (if applicable)