Computer Electronics
Computer Electronics
Lecture 4: Adder Circuits – Part 1

---
Outline
Outline
- The Arithmetic and Logic Unit (ALU)
- Representation of integer numbers
- Adder types:
  - Ripple carry adder
  - Carry select adder
- Worksheet

---
The Arithmetic and Logic Unit (ALU)
The Arithmetic and Logic Unit (ALU)
- The function of a computer is to compute
- Computations are performed by functional units
- The most important and versatile of the FUs is the ALU

---
Typical ALU operations
Typical ALU operations
- Arithmetic: Addition, subtraction
- Logical: NOT, AND, OR, XOR, …
- Less common (normally performed by dedicated FUs):
  - Bit shifting: left, right (logical or arithmetic)
  - Multiplication
  - Division

---
Why only simple operations?
Why only simple operations?
- Complex operations require more hardware whose cost must be justified
- Certain complex functions can be added as needed:
  - Dedicated IP cores integrated in the same chip
  - Dedicated chips integrated in the same board

---
The origin of the ALU
The origin of the ALU
- John von Neumann proposed it
- EDVAC computer, 1945

---
Integer number representation
Integer number representation
- Binary: easy to implement and robust to noise
- Resolution: number of bits
- Unsigned numbers: 0, 1, 2, …., N
- Signed numbers: -N/2, -N/2+1, -1, …, 0, +1, …, N/2-1

---
Unsigned numbers
Unsigned numbers

---
Signed numbers in 2’s complement
Signed numbers in 2’s complement

---
How to compute the 2’s complement
How to compute the 2’s complement
Method 1:
  - Invert all bits
  - Add 1
- Method 2:
  - Scan number from right to left
  - Up to the first 1 inclusively: leave unchanged
  - Invert all remaining bits
- Visualize in a circle

---
Adder circuits
Adder circuits
- Addition is the most basic arithmetic operation
- Basis for more complex operations, e.g. multiplication
- Different possible implementations
  - Simple implementation: small and cool but slow
  - Complex implementation: fast but big and power hungry
- Technology used influences architecture choice

---
Unsigned addition
Unsigned addition
Add 1010 = 10 base 10 and 0011 = 3 base 10
  1010
+0011
  1101
  0010 -> Carry
Overflow happens if
result < some operand
  1010 -> 10
+1010 -> 10
  0100 -> 4 (!)
  1010 -> Carry

---
Overflow
Overflow
Just check the last carry bit

---
Overflow pairs
Overflow pairs

---
Signed addition
Signed addition

---
Signed addition overflow
Signed addition overflow

---
Signed addition pairs
Signed addition pairs

---
Detect signed addition overflow
Detect signed addition overflow
- Adding 2 positive numbers results in negative number
- Adding 2 negative numbers results in positive number
- Can be checked by testing the last 2 carry bits
  - If they are equal (00 or 11) then no overflow
  - If they are different (01 or 10) then overflow

---
Unsigned vs. signed addition
Unsigned vs. signed addition
- Same adder supports both unsigned and signed
- Overflow detection logic different
  - Unsigned: Carry(n-1)
  - Signed: Carry(n-1) XOR Carry(n-2)

---
Ripple carry adder
Ripple carry adder

---
Half Adder (HA) truth table
Half Adder (HA) truth table
Inputs
Outputs
No input carry

---
Half adder logic circuit
Half adder logic circuit
Area: 2 gates
Delay: 1 gate

---
Full Adder truth table
Full Adder truth table
Input carry

---
Full Adder logic circuit
Full Adder logic circuit
- Area: 6 gates
- Propagation delay: 3 gate delays
Carry delays will add up!

---
Full Adder simplification
Full Adder simplification
- Area: 5 gates (1 less!)
- Delay: 3 gates (same)
Carry delays will add up!

---
FA transistor level implementation
FA transistor level implementation

---
Ripple carry adder
Ripple carry adder
Compute area and delay

---
RCA: compute unsigned overflow
RCA: compute unsigned overflow

---
RCA: compute signed overflow
RCA: compute signed overflow

---
RCA: advantage and disadvantage
RCA: advantage and disadvantage
- Advantage: simplest adder circuit, lowest area and power dissipation
- Disadvantage: it is slow
  - Delay is O(N), where N is number of bits
  - Carry computation is sequential:
    - Wait for C(i-1) to compute C(i)

---
Carry-select adder
Carry-select adder

---
CSA algorithm summary
CSA algorithm summary
- Split N bit addition into N/2 bit additions
- Use 1 RCA for lower part
- Use 2 RCAs for higher part
  - One assumes carry from lower part is 0
  - Other assumes carry from lower part is 1
- When carry from lower part available use it to select the correct higher part
- CSA delay is half RCA delay + mux delay
- Faster than RCA but bigger and more power hungry

---
K-stage CSA
K-stage CSA

---
Worksheet #4
Worksheet #4
Design a Full Adder circuit:
  1. Draw the symbol showing all inputs and outputs
  2. Write the truth tables for the outputs
  3. Design a logic circuit
2. Compute the area and delay of a 16-bit RCA that uses the FA of question 1.
  1. area = number of 2-input gates, delay = number of 2-input gates in critical path
3. Change the architecture to CSA to roughly quadruple the performance
4. Compute the area of the CSA of question 3.