Computer Electronics
Electronic Systems of Computers
Lecture 4: IOb-SoC Tour (continued) and first Verilog notions

---
IOb-SoC: recap of last lesson & more
Dual-Port
I/D
Memory
CPU
Wrapper
I/D
IBUS
DBUS
PBUS
ACCELERATOR BUS
UART BUS
User
Hardware
Accelerator
UART
[Speaker Notes: Let’s simplify the vNA.]

---
IOb-SoC: directories
- software: C/C++ software programs + python scripts for automation
- hardware: verilog hardware descriptions
- document: latex documents
- submodules: other repositories used by IOb-SoC, uses git submodule technology

---
IOb-SoC: the software directory
- Directories
  - firmware: the program to run on IOb-SoC (modify to create your own program)
  - bootloader: the resident bootloader program (do not edit)
- Files: (not intended to be edited)
  - software.mk: makefile segment for software makefiles
  - system.h: system parameters extracted from configurations entered in .mk files
  - template.lds: linker script

---
IOb-SoC: linker script
SECTIONS {
        .memory : {
        . = 0x000000;
        *(.init);
        *(.text);
        *(*);
        . = ALIGN(4);
        _heap_start = .;
        end = .;
        }
}
.init
(this code section is declared
in the code itself)
.text
(all other unidentified code sections)
Statically allocated data
(global and local static variables)
Dynamically
allocated data

---
IOb-SoC: the firmware directory
- Files (visit & understand)
  - Makefile: firmware top build script
    - Includes software.mk
  - firmware.S: the assembly start file
    - Includes system.h
  - firmware.c: the firmware C program
    - Includes system.h

---
IOb-SoC: bootloader and console
- Bootloader
  - Same structure as firmware
    - it is a normal program but used to boot the system
- Console (submodules/LIB/software/python/console)
  - Communicates with the target where IPb-SoC is running
    - Board: USB/RS232 (UART)
    - Simulator: files cnsl2soc and soc2cnsl
  - May send the firmware to target repeatedly for debugging without hardware recompilation
  - Acts like a server and the target is the client asking it to print messages, send or receive files and terminate execution

---
IOb-SoC: the hardware directory
- Directories
  - src: the basic system verilog files
  - testbench: Verilog testbench
  - include: the Verilog header files (shared by many files)
  - simulation: build and run directories
  - fpga: build and run directories
  - asic: build and run directories
- Files:
  - hardware.mk: makefile segment for hardware makefiles (simulation, fpga and asic)

---
IOb-SoC: the hardware/src directory
- Contains Verilog modules
- Verilog is a hardware DESCRIPTION language
- Verilog is not a programming language
- We are describing circuits not procedures
- We use procedures to describe circuits

---
Testbench and Unit Under Test (UUT)
Verilog module
(a digital circuit)
Verilog module
A Digital Circuit
Inputs
Outputs
Inouts (bidirectional wires)

---
Verilog module (a real circuit)
module my_peripheral
   (
    input clk,
    input rst,
    // native bus
    input valid,
    input [`SRAM_ADDR_W-3:0] addr,
    input [`DATA_W-1:0] wdata, //used for booting
    input [`DATA_W/8-1:0] wstrb, //used for booting
    output [`DATA_W-1:0] rdata,
    output ready
);
//description of module goes here
endmodule

---
The testbench directory
The testbench
Output
Signal analyzers
Input
UUT
Pass/Fail
Signal sources

---
Verilog testbench
(not a real circuit!)
Used in Verilog simulation!
module my_testbench;
//description of test hardware
//instance of the Unit Under Test
endmodule

---
Verilog header files
`include “my_header_file.vh”
// this like the C language #include
module my_testbench;
//description of test hardware
//instance of the Unit Under Test
endmodule

---
IOb-SoC: the simulation directory
- Contains simulation build and run directories, one directory per simulator
  - Only the icarus simulator will be used
    - The icarus directory only has a simulation makefile (visit)
- Files:
  - the simulation.mk makefile segment (visit)
  - The waves.gtkw input file for the gtkwave program

---
IOb-SoC: the document directory
- Contains document build directories, one directory per document type
  - pb: product brief
    - Makefile
    - .tex files
    - .pdf file for easy viewing
    - Private figures directory
  - presentation: slide presentation
- Contains the figures directory
  - Figures that are shared among different documents

---
IOb-SoC: the submodules directory
- System submodules
  - CPU
  - CACHE
  - UART
- A git submodule is a pointer to another git repository
  - Allows for modular and distributed development
  - Easy to add with the git submodule add <url> path/to/the/submodule
  - Easy to remove: git rm path/to/the/submodule
- The way the system collects hardware and software components from the submodules and assembles them in the system is taught in the next class.