Computer Electronics
Computer Electronics
Lecture 16: Dynamic Random Access Memory (DRAM)

---
Outline
Outline
- DRAM cell
- DRAM matrix
- DRAM read
- DRAM write
- DRAM high-level operation
- DRAM module organization
- DRAM refresh
- Real DRAM chips

---
DRAM Cell
DRAM Cell

---
DRAM cell matrix
DRAM cell matrix

---
DRAM Reading  problem
DRAM Reading problem
- Select Row using address
- Cell charge has little effect on line voltage Vd because Cc << Cd
- Final voltage Vf=(Cd*Vd+Cc*Vc)/(Cd+Cc)
    Vf = Vd+Cc/Cd Vc
- For Cc=40fF, Cd=1pF, Vc=5V then the variation is only 200mV
- Since the transistors leak current then variation is even smaller
- Difficult to detect this small variation!
Cc
Cd

---
Solving the read problem
Solving the read problem
1. Use complementary bit lines to store d and ~d (doubles circuit area, not necessary but eases explanation)
2. Pre-charge the bit lines at Vdd/2
3. Select Row:
Vd=Vdd/2+ΔV/2 and V~d=Vdd/2-ΔV/2
1. Amplify ΔV using sense amp
2. Select Column to read data

---
Pre-charge complementary bit lines
Pre-charge complementary bit lines
d
~d
Vdd/2
Voltage equalization circuit
Pre-charge enable
(disable after complete)

---
Select row, sense and read
Select row, sense and read
d
~d
Select Row:
Vd=Vdd/2+ΔV/2 and V~d=Vdd/2-ΔV/2
1. Amplify ΔV using sense amp – This also restores the cells!
2. Select Column to read data
Select Row
Power Up
Sense Amp
Select Column

---
DRAM high-level view
DRAM high-level view

---
DRAM timing diagram
DRAM timing diagram

---
DRAM fast page mode
DRAM fast page mode

---
DRAM Extended Data Output (EDO)
DRAM Extended Data Output (EDO)
Uses register to hold previously read data while new data is read
Pipelined access!

---
Burst Extended Data Output (BEDO)
Burst Extended Data Output (BEDO)
Column address is incremented internally for greater speed!

---
Synchronous (SDRAM)
Synchronous (SDRAM)
Synchronous operation facilitates external generation of signals
Column address still incremented internally like BEDO

---
Double Data Rate (DDR)
Double Data Rate (DDR)
Like SDRAM but data made available at both clock edges
Bandwidth is doubled!

---
Configuring CPU to use some DRAM
Configuring CPU to use some DRAM
Note that cycle time is given by
tRAS=tRP+tRCD+tCL

---
Memory module organization
Memory module organization

---
Serial presence detect
Serial presence detect
- Modules have a small chip to inform whether they are present
- Useful in Power On Self Test (POST)

---
DRAM refreshing
DRAM refreshing
- Cell transistors leak and there’s nothing we can do about it
- Cell needs refreshing before stored info is gone
- When a cell is read it is restored (refreshed)

---
DRAM refresh modes
DRAM refresh modes
- RAS only
- CAS before RAS
- Hidden

---
RAS only refresh
RAS only refresh
address
data
Provide Row address and activate RAS
No need to activate CAS

---
CAS before RAS refresh
CAS before RAS refresh
No need to provide Row address (incremented internally)
This is signaled by activating CAS before RAS

---
Hidden refresh
Hidden refresh
- Performs refresh while data is output
- Reduces refresh overhead

---
Refresh overhead
Refresh overhead
- Refresh interval: every row must be refreshed within this interval
- Refresh time: time to refresh all rows
- Overhead = refresh time/refresh interval

---
A real example
A real example

---
Datasheet values
Datasheet values

---
Watch this Youtube video
Watch this Youtube video
- https://www.youtube.com/watch?v=8zhr72a6tqQ
- By Prof. Amitava Dasgupta, Department of Electrical Engineering, Indian Institute of Technology, Madras.