Computer Electronics
Computer Electronics
Lecture 19: Add-Shift Multiplier, Divider and Shifter Circuits

---
Add-shift multiply: fundamentals
Add-shift multiply: fundamentals
- Use accumulator register
- Successively add and shift the partial products
- Multiplication ready after N partial products are accumulated
- One accumulation per clock cycle

---
Add-shift signed multiply: circuit
Multiplicand
register (n)
zeroer
n
i==n
inverter
n
Counter
adder
cin
n
n+1
Product-Multiplier (PM)
Right-Shift register (2n bits)

---
Add-shift signed multiply: example
Add-shift signed multiply: example
M=-710=1001 , m=210=0010
M*m = -1410 = 11110010
Clock cycle	Product /multiplier reg	Comments
0	00000010	Initial: P=0, m=0010
1	00000001	Nop, SRA
2	11001000	Add M, SRA
3	11100100	Nop, SRA
4	11110010	Subtract M, SRA

---
Division algorithm
Division algorithm
				1	1	1	0		0	0	1	1
-	0	0	1	1					0	1	0	0
		0	0	1	1
	-	0	0	1	1
			0	0	0	1
		-	0	0	1	1
				0	0	1	0
			-	0	0	1	1
				0	0	1	0
		1	4		0	3
-	0	3			0	4
		1	4
	-	1	2
		0	2
Dividend: 14 or 1110
Divisor: 3 or 11
Quotient: 4 or 100
Remainder: 2 or 10

---
Matrix divider
Matrix divider

---
Subtract-shift divider: fundamentals
Subtract-shift divider: fundamentals
Very similar to add-shift multiply
  - Same circuit with few additions does both
- Successively subtract divisor from current remainder and shift left
- Division ready after N subtractions are accumulated
- One accumulation per clock cycle

---
Subtract-shift divider: circuit
Subtract-shift divider: circuit
Divisor reg (n bits)
Cout
Adder
Cin = ‘1’
1
0
Remainder/Quotient reg (2n bits)
Shift left every cycle

---
Subtract-shift divide: example
Subtract-shift divide: example
Clock cycle	Remainder/quotient reg	Comments
0	00001110	Initial: r=0000, D=1110
1	00011100	No Sub, SL, q3=0
2	00001001	Sub d, SL, q2=1
3	00010010	No Sub, SL, q1=0
4	00100100	No Sub, SL, q0=0
D=14, d=3 D=1110, d=0011
D/d = q =4, D%d = r = 2, q=0100, r=0010

---
Bit shifting
Bit shifting
- Left or right bit shifting is a useful operation
- 1-bit shifting can be accomplished with a shift register
- N-bit shifting is accomplished with a barrel shifter circuit

---
Single bit shifting
Single bit shifting
Legend
l/r: left/right
L/A: logical/arithmetic
L/A select
‘0’
L
A
r
r
r
r
l
l
l
l
FFD
FFD
FFD
FFD
‘0’
l/r select

---
Shifting types (1-bit displace)
Shifting types (1-bit displace)
- Left: b0 <= 0, bi <= bi-1
- Left circular: b0 <= bn-1, bi <= bi-1
- Right logical; bn-1 <= 0, bi-1 <= bi
- Right Arithmetic: bn-2 <= bn-1, bi-1 <= bi
- Right circular: bn-1 <= b0, bi-1 <= bi

---
Barrel shifting (d-bit displacement)
Barrel shifting (d-bit displacement)
- Displace by d bits left or right
- Circular or not
- Arithmetic or logical if right shift

---
Barrel shifter using multiplexers
Barrel shifter using multiplexers
- Spatial complexity O(N*logN)
- Right logical

---
Barrel shifter using transistor matrix
Barrel shifter using transistor matrix
- Spatial complexity O(N2)
- Right arithmetic

---
Transistor matrix BS – layout
Transistor matrix BS – layout
Most space taken by interconnects rather than transitors