Computer Electronics
Computer Electronics
Lecture 9: Dedicated Processors

---
Why design a dedicated processor
Why design a dedicated processor
- Not needed for anything else
- No or limited programmability needed
- Can reduce cost in volume production
- Can reduce power/energy consumption
- Better form factor (size matters)
- Has a simpler user interface

---
Dedicated processors combined with GPPs
Dedicated processors combined with GPPs
- PCIe cards
- Graphics cards
- Surveillance equipment
- Audio equipment
- Etc.

---
Design of dedicated processors
Design of dedicated processors
Data and control paths

---
Design methodology or Art
The Art of Design
- Describe the algorithm in a high-level text description
- Draw the datapath
- Write the pseudo-code for the control path (normally a FSM)
- Make sure you list:
  - IO signals: name, width, direction (I,O,IO), description
  - Registers: name, address, direction (Read, Write, RW), description
  - Memories: name, function (instructions, data, ..), volatile/non volatile, type (ROM,EPROM,RAM,reg file), internal/external, ports (single, dual, two-port, dual-port
    - Holy Grail of Computing: N-port memory!!
  - Data streams: name, description, width, continuous/interrupted
  - Buses: name, purpose, type (Native, AXI, Wishbone, ISA, …)
- Draw timing diagrams (use wavedrom, simulation of small circuits)

---
Design example: dedicated processor that computes pq
Design example: dedicated processor that computes pq
- p is a streaming input (volatile in C language)
- Textual description already given
- Many possible architectures
- Many possible trade-offs…
- Let’s get to the block diagram

---
Parallel architectures
Parallel architectures
p
p
X
X
X
X
X
X
q mults
X
X
X
Tree structure
Linear array
Same throughput lower latency

---
Data valid signals
Data valid signals
Interesting online tool: http://wavedrom.com/editor.html

---
Propagation of the valid signal
Propagation of the valid signal
p
p
X
X
X
X
X
X
q mults
X
Distributed light control
X
X
Tree structure
Linear array
Same throughput lower latency

---
Parallel architecture: software accessible registers
- Register p: write-only, 16 bits for example
- Register q: write-only, 16 bits for example
- Register r (result): read-only, 32 bits for example
- Result comes fast: start and done registers may be dispensed with

---
Serial architecture: block diagram
Serial architecture: block diagram
fifo_in_write
Multiplier
FIFO_IN
x=p
fifo_full_full
fifo_in_empty
fifo_in_read
cnt_start
Counter
Control
rst_reg
cnt_en
cnt_done
reg (q*W bits)
reg_en
reset
fifo_out_write
fifo_out_full
fifo_out_empty
FIFO
y=pq
reg_out
fifo_out_read

---
Serial architecture: software accessible registers
- Register p: write-only, 16 bits for example
- Register q: write-only, 16 bits for example
- Register r (result): read-only, 32 bits for example
- Result comes several clock cycles later, especially if q is large:
  - Start (1 bit, write-only) and Done (1 bit, write-only) registers are advisable
  - Alternatively, the timer can be used to wait for exactly the time the calculation will take

---
Design control circuit
Design control circuit
- Flowchart … better for software
- State transition diagram or table
- Pseudo-code
- Experienced designer: HDL (Verilog, VHDL, etc)

---
Controller canonical form
Controller canonical form
Inputs
Combinatorial circuit
Outputs
Current state
State register
Next state

---
State transition diagram
State transition diagram
fifo_in_empty=1
reset=1
(reg=1, cnt=0)
Unknown
Init
fifo_in_empty=0/fifo_in_read=1, reg_en=1,
cnt_start=1, cnt_en=1
Accumulate
fifo_in_empty=1/reg_en=0,
        cnt_en=0
cnt_done=0,fifo_in_empty=0/
cnt_start=1, rst_reg=1,
Pause
fifo_in_empty=0/
fifo_in_read=1,
cnt_en=1, reg_en=1
cnt_done=1, fifo_in_empty=1/
reg_en=0, cnt_en=0

---
State transition table (very incomplete… no space!)
State transition table (very incomplete… no space!)
state	Inputs				Outputs			Next state
st	reset	cnt_done	fifo_in_empty	fifo_out_full	fifo_in_read	fifo_out_write	Reg_en	nxt_st
?	1	-	-	-	-	-	-	init
Init	0	0	1	0	0	0	0	init
Init	0	0	0	0	1	0	0	Accumulate
Accumulate

---
Next steps
  `SIGNAL(pc, 3)
  `SIGNAL(pc_next, 3)
   `REG_AR(bclk, rst_bclk, 3'b0, pc, pc_next)
   `COMB begin
      //default assignments
      pc_next = pc+1'b1;
      rst_reg = 1’b0;
      start_counter = 1’b0;
      en_counter = 1’b0;
      …
     case(pc)
        0: if (!START) begin //wait for sw start
        pc_next = pc;
        1: if (fifo_in_empty)
        pc_next = pc;
        else begin
        rst_reg = 1;
        start_counter = 1;
        end
        2: begin
        en_reg = 1;
        en_counter = 1;
        3: if (counter != q)
        pc_next <= 1;
       default: begin
        pc_next <= pc;
        done <= 1;
      endcase;
 end // `COMB
Write finite state machines that look like assembly programs!
This program or FSM does not work,
only good for teaching ==>

---
Next steps
- Write HDL code (say Verilog) and simulate
- Run synthesis
  - Compiles Verilog and produces a generic netlist (gates and flip-flops not related to any technology)
- Run mapping
  - Converts generic netlist into technology dependent netlist using a component library
- Run place and route
  - Places cells and wire connections into layout
- If user time constraint violations tweak design or tool options and rerun
- Complex tools: full configuration requires scripting (in tcl normally)
- A competent designer or design manager can earn a few hundred K/year