Computer Electronics
Computer Electronics
Lecture 15: Adder Circuits – Part 1

---
Typical ALU operations
Typical ALU operations
- Arithmetic: Addition, subtraction
- Logical: NOT, AND, OR, XOR, …
- Less common (normally performed by dedicated FUs):
  - Bit shifting: left, right (logical or arithmetic)
  - Multiplication
  - Division

---
Why only simple operations?
Why only simple operations?
- Complex operations require more hardware whose cost must be justified
- Complex functions can be decomposed as a time sequence of simple operations
- Certain complex functions can be added as needed:
  - Dedicated IP cores integrated in the same chip
  - Dedicated chips integrated in the same board

---
The origin of the ALU
The origin of the ALU
- John von Neumann proposed it
- EDVAC computer, 1945

---
Integer number representation
Integer number representation
- Binary: easy to implement and robust to noise
- Resolution: number of bits, N
- Unsigned numbers: 0, 1, 2, …., 2N-1
- Signed numbers: -2N-1, -2N-1+1, …, -1, 0, +1, …, 2N-1-1
- Signed numbers: 2’s complement representation normally used

---
How to compute the 2’s complement
How to compute the 2’s complement
- Method 0: (software)
  - complement2two(x) = 2N-x
- Method 1: (hardware)
  - Invert all bits
  - Add 1
- Method 2: (hand, hardware?)
  - Scan number from right to left
  - Up to the first 1 inclusively: leave unchanged
  - Invert all remaining bits
0000
0001
1111
0010
1110
13+6=3!
1101
0011
0100
1100
1011
0101
1+5=6
0110
1010
0111
1010
1000

---
Adder circuits
Adder circuits
- Addition is the most basic arithmetic operation
- Basis for more complex operations, like multiplication, division, etc
- Different possible implementations
  - Simple implementation: small and cool (low power), high combinational delay
  - Elaborate implementation: big and hot (high power), low combinational delay
- Technology used influences architecture choice
  - FPGA use the simplest, for example

---
Unsigned addition
Unsigned addition
Overflow happens if
result < some operand
  1010 -> 10
+1010 -> 10
  0100 -> 4 (!)
  1010 -> Carry
1010+0011=1010+310
  1010 → 10
+0011 → 3
  1101 → 13
  0010 -> Carry

---
Overflow
Visualizing and computing unsigned addition and overflow
0000
10 + 12 = 6!
  1010
+1100
--------
  0110
  1000 → carry on MSB is overflow
0001
1111
0010
1110
13+6=3!
1101
0011
0100
1100
1011
0101
1+5=6
0110
1010
0111
1010
1000

---
Signed addition
Signed addition
Overflow happens if addition of 2 positives (negatives) is a negative (positive)
  1010 → -6, negative
+1011 → -5, negative
--------
  0111 → 7!, positive!
  1010 → carry
-3 - 2 = -5
  1101
+1110
--------
  1011
  1100 → carry

---
Visualizing and computing signed addition and overflow
How to flag signed addition overflow in hardware?
Overflow = (result_sign XOR a_sign)
AND (a_sign XNOR b_sign)
Equivalent to
Overflow = C(n-1) XOR C(n-2)
Can you prove this?
0000
0001
1111
0010
-1+2=1
1110
1101
0011
4+7=-5!
0100
1100
1011
0101
0110
-4-6=6!
1010
0111
1010
1000

---
Unsigned vs. signed addition
Unsigned vs. signed addition
- Same adder hardware is used!!
  - Greatest advantage of 2s complement!
  - Unsigned and signed interpreted differently but addition operation is the same
- Overflow detection
  - Unsigned: Carry(n-1)
  - Signed: Carry(n-1) XOR Carry(n-2)

---
Ripple carry adder
Ripple carry adder

---
Half Adder (HA) truth table
Half Adder (HA) truth table
No input carry
s_i = a_i overline {b_i} + overline {a_i}b_i = a_i oplus b_i
c_{i+1} = a_i b_i
Inputs
Outputs

---
Half adder logic circuit
Half adder logic circuit
s_i = a_i overline {b_i} + overline {a_i}b_i = a_i oplus b_i
c_{i+1} = a_i b_i
Area: 2 gates
Delay: 1 gate

---
Full Adder truth table
Full Adder truth table
Inputs
Outputs
Input carry
s_i = a_i oplus b_i oplus c_i
c_{i+1} = a_i b_i + ( a_i + b_i )c_i
a_i b_i = g_i
Generate
a_i + b_i = g_i
Propagate

---
Full Adder logic circuit
Full Adder logic circuit
- Area: 6 (2-input) gates
- Propagation delay: 3 gate delays
Carry delays will add up when blocks chained!

---
Full Adder simplification
Full Adder simplification
c_{i+1} = a_i b_i + ( a_i + b_i )c_i newline c_{i+1} = a_i b_i + ( a_i oplus b_i + a_i b_i)c_i newline c_{i+1} = a_i b_i(1+c_i) + ( a_i oplus b_i)c_i newline c_{i+1} = a_i b_i + ( a_i oplus b_i)c_i
- Area: 5 gates (1 less!)
- Delay: 3 gates (same)
Carry delays will add up!

---
Ripple carry adder
Ripple carry adder
Compute area and delay

---
RCA: compute unsigned overflow
RCA: compute unsigned overflow

---
RCA: compute signed overflow
RCA: compute signed overflow

---
RCA: advantage and disadvantage
RCA: advantage and disadvantage
- Advantage: simplest adder circuit, lowest area and power dissipation
- Disadvantage: it is slow
  - Delay is O(N), where N is number of bits
  - Because carry computation is sequential:
    - Wait for C(i-1) to compute C(i)

---
Carry-select adder
Carry-select adder

---
CSA algorithm summary
CSA algorithm summary
- Split N-bit addition into N/2-bit additions
- Use 1 RCA for lower part (A)
- Use 2 RCAs for higher part (B and C)
  - B assumes carry from lower part is 0
  - C assumes carry from lower part is 1
- Carry A selects the output from either B or C, which had been computed in parallel with A
- CSA delay is half RCA delay + mux delay
- CSA is 100% faster than RCA but 50% larger

---
K-stage CSA
Example 32-bit/4-stage:
A(CSA)/A(RCA)= (32+24)FA/32FA = 7/4
Delay(RCA) / Delay(CSA) = 32FA/8FA= 4
K-stage CSA