Computer Electronics
Computer Electronics
Lecture 7: Digital Circuits using Verilog and IOb-Lib

---
Modular circuit design
Module
Submodule B
Submodule A
OUTPUTS
Wires
Submodule C
Submodule D
INPUTS

---
IOb-lib: module interface
module my_module (
      `INPUT(X, 8), //declare 8-bit input
      `INPUT(Y, 8),
      `OUTPUT(Z, 16) //declare 16-bit output
      `INOUT(F, 32) //declare 32-bit bidirectional port
   );
   <module body>
endmodule

---
Instantiate sub-components
module my_module
(
 //module ports
...
);
...
   my_submodule comp0
   (
      .X(A),
      .Y(B),
      .Z ( C),
      .F (D)
  )
...
endmodule
my_module
my_submodule
comp0
A
B
X
Y
Z
C

---
Wires and variables
- Circuits are blocks connected by wires that carry digital signals (0 or 1)
- So we need to declare and use wires
- Verilog describes two types of wires:
  - Type wire: used for connections and assign statements
  - Type reg: user for operation results within always and initial processes
- Using IOb Verilog macros:
  - Type wire: `IOB_WIRE(NAME, WIDTH)
  - Type reg: `IOB_VAR(NAME, WIDTH)
- Signed versions:
  - Type wire: `IOB_WIRE_SIGNED(NAME, WIDTH)
  - Type reg: `IOB_VAR_SIGNED(NAME, WIDTH)

---
Typical module: combinatorial
circuit plus register
Inputs
`IOB_COMB
Outputs
iob_reg
Current state
Next state

---
IOb-lib: registers!
Inputs
Combinatorial circuit
Outputs
Register
Current state
Next state

---
IOb-lib: registers
- IOb-lib users are not allowed to describe registers in Verilog (allowing tools to infer them)
- IOb-lib users must instantiate the iob_reg component

---
The iob_reg module
`timescale 1ns / 1ps
module iob_reg
  #(
    parameter DATA_W = 0,
    parameter RST_VAL = 0
    )
   (
    input clk,
    input arst,
    input rst,
    input en,
    input [DATA_W-1:0] data_in,
    output reg [DATA_W-1:0] data_out
    );
   //prevent width mismatch
   localparam [DATA_W-1:0] RST_VAL_INT = RST_VAL;
   always @(posedge clk, posedge arst) begin
      if (arst) begin
        data_out <= RST_VAL_INT;
      end else if (rst) begin
        data_out <= RST_VAL_INT;
      end else if (en) begin
        data_out <= data_in;
      end
   end
endmodule
Exercise: instantiate a register

---
IOb-lib: combinatorial circuits
Inputs
Combinatorial circuit
Outputs
Register
Current state
Next state

---
Combinatorial blocks
`IOB_COMB is defined in iob_lib.vh:
`define IOB_COMB always @*
What is always @*?
The verilog explanation is cumbersome
The iob-lib explanation is trivial:
1) `IOB_COMB describes a combinatorial block
2) LHS are computed variables using wires and other variables
3) RHS are inputs: wires or other variables
4) computed variables need to be converted to wires to be used for interconnection
module my_module
(
 //interface signals
);
...
   `IOB_VAR(zv,10);
   `IOB_VAR(yv,10);
   `IOB_COMB begin
       //insert C-like expressions here: examples
       zv = s? X: Y;
       yv = a*(b+c);
   end
`IOB_VAR2WIRE(zv, z)
`IOB_VAR2WIRE(yv, y)
...
endmodule
WARNING: make sure you have
no feedback loops

---
Order of statements
In Verilog the order of statements is irrelevant since we are merely listing components
However:
Signal declarations must precede their use
Inside a combinatorial block, the order of statements is important because it is described procedurally
Only the variables computed in a combinatorial block matters and this computation may be affected by the order of statements

---
Combinatorial block: if statements
module my_module
(
 //interface signals
);
...
   `IOB_VAR(zv,10);
   `IOB_COMB begin
   zv = y;
   if (s)
       zv = x;
   end
`IOB_VAR2WIRE(zv, z)
...
endmodule
module my_module
(
 //interface signals
);
...
   `IOB_VAR(zv,10);
   `IOB_COMB begin
   if (s)
       zv = x;
   else
       zv = y;
   end
`IOB_VAR2WIRE(zv, z)
...
endmodule

---
Combinatorial block: for loops
module my_module
(
 //interface signals
);
…
   integer	i;
   `IOB_VAR(c,9);
   `IOB_VAR(s,8);
   `IOB_COMB begin
   for (i=0; I<N; i=i+1)
       s[i] = a[i] ^b[i] ^c[i];
       c[i+1] = a[i]&b[i] | ( c[i] & (a[i] ^b[i] ));
   end
`IOB_VAR2WIRE(y, s)
`IOB_VAR2WIRE(co, c[8])
...
endmodule