Computer Electronics
Computer Electronics
Lecture 2: Introduction to IOb-SoC and Verilog

---
Recap of last lesson
John von Neumann
CPU
Processor Bus
MASTER
SLAVES
Output bus
BUS SPLIT
Input bus
Output
Devices
Output
Devices
Output
Devices
Output
Devices
Output
Devices
Output
Devices
Output
Devices
Output
Devices
Input
Devices
Output
Devices
Memory
Accelerators’ bus
Output
Devices
Output
Devices
Output
Devices
Output
Devices
Compute
Devices
Memory bus
[Speaker Notes: Let’s simplify the vNA.]

---
The Processor Bus
Processor buses can be complex, for example ARM’s AXI
In this course a minimalistic yet effective 6-signal bus called the Native Bus will be used:
Signal Name	Direction wrt CPU	Width in bits (wires)	Description
Valid	Output	1	CPU wants to access data or instructions
Address	Output	32	Address of the data
Wdata	Output	32	Data to write
Wstrb	Output	4	Byte write
Rdata	Input	32	Data read
Ready	Input	1	Slave is ready
REQUEST
RESPONSE
[Speaker Notes: Let’s simplify the vNA.]

---
Master reading from slave
[Speaker Notes: Let’s simplify the vNA.]

---
Master writing to slave
[Speaker Notes: Let’s simplify the vNA.]

---
System on Chip & IP Cores
IP Core providers design IP cores: ADC, MCU, PWM, etc
Fabless Integrated Circuit providers integrate IP cores and make the SoC (AMD, Xilinx, etc)
Foundries fabricate SoCs and other chips
[Speaker Notes: Let’s simplify the vNA.]

---
System on Chip
- The SoC is an IP core assembly
- The whole system sits on a single chip
- Less components on Printed Circuit Boards
- Less weight and volume
- More performance
Lower power consumption

---
Iob-SoC block diagram
- Developed by IP core provider IObundle Lda with the help of master students students (Roque,Silva,Ratinho,Mário, …, Internships/Dissertations)
- Simple SoC comprising
  - The PicoRV32 RISC-V CPU (open-source)
  - Boot ROM (has small program to load user programs)
  - SRAM (on-chip memory for running small programs or storing fast access data)
  - Instruction and Data L1 Caches + shared L2 cache
  - UART interface for communication
  - Other optional modules

---
Getting hands dirty on IOb-SoC
- Hosted by Github
- Read the README file
- Clone the repository
- Move into its directory
- Simulate the design and visualize simulation waveforms
- Make the document

---
Git in a few slides
- Developed by Linus Torvalds (also Linux creator)
- Managing your project files efficiently
- Reduce storage and backup needs
- Manage different versions and development branches in large teams
- Access the project files anywhere
- Successor of CVS, SVN but better

---
The cloud
remote
server
remote
server
remote
server
Push
Pull
edge
device
edge
device
edge
device
The edge

---
Meanwhile and the Edge
repository
(directory)
user
file
user
directory
.git
(directory)
Checkout
user
directory
user
directory
user
directory
user
directory
The index
The tree
(or Plato’s Cave!)
(or Real Thing)

---
Common git commands
- git config –global user.name “your name”
- git config –global user.email “your@fantastic.email”
- git init: turns directory into git repository
- git status: shows differences to index
- git add: stages the files to be commited in index
- git commit: creates a new development node (commit or hash)
- git push: sends your commits to a remote
- git branch: creates a development branch

---
Development branches
- Develop each feature in a branch
- Test / Fix
- Merge with master branch
- Retest / Fix
- Release!

---
Common git commands
- git log: shows commit history
- git fetch: downloads branches from a remote
- git pull: same as git fetch + git merge
- git show: shows contents in any commit
- git remote: shows remote servers in use
- After you get up: eat breakfast then do git pull (update your repo)
- Before you go to bed: do git push (save your work) and brush your teeth

---
The Make utility program
- Make is a program that automates the process of building programs (compiling)
- Created by Steward Feldman in 1976
  - Also wrote the first Fortran 77 compiler
  - Part of the Bell Labs team who created the Unix operating system, the precursor of Linux for masses
- Make is still one of the best buid automation tools!